## Slide 1: ASEAN GMP TRAINING MODULE QUALITY CONTROL
Prepared by :
Stephanie Wong Choong Moy ~ Malaysia
Eusebia Regodon ~ Philippines
Approved by
ASEAN GMP Team
Endorsed by
ASEAN Cosmetic Committee

## Slide 2
Introduction
  Objective
  Scope
Quality Control Principle
  QC Overview
  QA versus QC
  General Principle
Basic Requirement of Quality Control
  Quality control unit
  Quality control laboratory
  Responsibility
Quality Control Documents
Tasks of Quality Control
References
CONTENT OF PRESENTATION
Notes: <number>
<footer>
<header>
<date/time>
Content description :
Introduction :
  Objective
  Scope
Quality control principle
  QC overview
  QA versus QC
  General principles
  Quality control unit
Basic requirement of quality control
  Basic responsibilities
  Other responsibilities
Tasks of quality control department
  Quality control work flow
  Material receipt
  Sampling guidance
  Testing and analysis
  Reagent management
  Calibration
  Stability study
  Retained samples
  Contract analysis
  Reprocess handling
  Returned good handling
  Environment monitoring
Quality control documents
Definition
QC Overview
Scope
General Principles
Responsibility
Quality Control Laboratory
Specification Control
In-Process Quality Control
Laboratory Documentation and Retention
Starting Materials and Packaging
Receipt
Sampling
Testing
Control of Starting/Packaging Materials Acceptance
Control of Process Water Acceptance
Control of Finished Product Acceptance
Out of Specification Investigation
Laboratory Reagent
Environment Monitoring
Stability Study
Calibration
Sub-contracting of Test and Calibration
Reprocessing
Return
Reference

## Slide 3
INTRODUCTION

## Slide 4
INTRODUCTION
Good Manufacturing Practice (GMP) is the part of Quality Assurance that ensures that products are produced and controlled consistently and reliably. This consistency of production and control is essential. It can only come about by having clear descriptions of the way in which the work will be done.
GMP specifically addresses risks of cross-contamination and mix-up that cannot be fully controlled by testing of the final product.
These risks can best be controlled by having a properly managed system of working that takes them into account. This means that the quality checking system must be designed with these risks in mind and set out to find whether any errors have occurred.
Notes: Fitness for intended use
  Safe
  Effective
Consistency
  Process
  Product
Fitness for intended use
  Safe
  Effective
Consistency
  Process
  Product

## Slide 5
To understand key elements in quality control.
To understand specific requirements on organization, procedures, processes and resources.
OBJECTIVES
Notes: <number>
<footer>
<header>
<date/time>
It provides assurance that cosmetic products will be of consistent quality appropriate to their intended use.

## Slide 6
SCOPE
Quality control involved sampling, inspecting and testing of starting materials, in process, intermediate, bulk and finished products.
It also includes where applicable, environment monitoring program, review of batch documentation, sample retention programs, stability studies and maintaining correct specification of materials and products.
Notes: <number>
<footer>
<header>
<date/time>
The examination of output data to ensure that it has been properly processed and meets established accuracy standards
Inspection, analysis and action applied to a portion of the product in a manufacturing operation to estimate overall quality of the product and determine what, if any, changes must be made to achieve or maintain the required level of quality
A procedure for keeping quality of inputs or outputs to specifications
Those actions that control the attributes of analytical process, system, or facility according to predetermined quality requirements

## Slide 7
QUALITY CONTROL PRINCIPLES

## Slide 8
Sampling
Inspection & testing of: Starting Material, Bulk, Intermediate, Finished product
Environment monitoring program
Batch record review/documentation
Sample retention program
Stability study
Calibration
Reagent Handling
Release/Reject: Control for materials & product disposition
QUALITY CONTROL OVERVIEW
Return
How
Reprocessing
Product with consistent quality for its intended use
Assurance
Established Quality System Requirements
Product contain the correct materials of specified quality & quantity
Manufactured under proper conditions accordingly to SOPs
Specification Control
Key
Focus
Area
Objective

## Slide 9
The terms quality assurance and quality control are often used interchangeably to refer to the actions performed for ensuring the quality of a product, service, or process.
Both terms, however, have many interpretations because of the multiple definitions for the words "assurance" and "control."
The definitions below, for example, point toward a specific distinction between these two terms:
Assurance = The act of giving confidence, the state of being certain, or the act of making certain.
Assurance : The act of giving confidence, the state of being certain, or the act of making certain.
Quality assurance : All the planned and systematic activities implemented within the quality system that can be demonstrated to provide confidence a product or service will fulfill requirements for quality.
Control : An evaluation to indicate needed corrective responses; the act of guiding or the state of a process in which the variability is attributable to a constant system of chance causes.
Quality control :The operational techniques and activities used to fulfill requirements for quality.
QA VS QC
Notes: This comparison is provided by ASQ (American Society of Quality)

## Slide 10
Each holder of a manufacturing authorization should have a QC Department
Independence from production and other departments is considered to be fundamental
Under the authority of an appropriately qualified and experienced person with one or several control laboratories at his or her disposal.
If do not have any facility, it can be managed by appointed respective external laboratory institution(s).
GENERAL PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
General principles:
QC department is needed to ensure that products contain the correct materials of specified quality and quantity are manufactured under proper conditions according to standard written procedures.
Each manufacturing unit should have QC department with their own laboratory unit that oversees production operation to ensure quality product is produced
The independence of quality control from production is considered fundamental. The quality control department should be independent from other departments
Under the authority of a person with appropriate qualifications and experience, who has one or several control laboratories at his disposal.
If the manufacturer do not have any laboratory, they can manage to have contract analysis with respective laboratory institution(s).

## Slide 11
BASIC REQUIREMENTS OF
QUALITY CONTROL

## Slide 12
Quality Control department should have :
resources:
  adequate facilities
  qualified personnel
  approved written procedures
tasks :
  sampling, inspecting, testing,
  releasing or rejecting
  monitoring
objects :
  Starting materials, intermediates, bulk, and finished products
  Returned products
  Environmental conditions
BASIC REQUIREMENTS
Notes: <number>
<footer>
<header>
<date/time>
QC department should have :
Resources availability to carry out QC activities
  Adequate laboratory facilities or access to them e.g. government or contract laboratories
  Appropriately qualified, trained and experienced personnel
  Establish standardized test methods and specifications
The operational tasks of the quality control department are:
  Sampling, inspecting, and testing of all starting materials, packaging materials, intermediates, bulk products, finishes products, and also returned products, which should be done by personal with method and plan approved by QC. Records are made, manually and/or by recording instruments, which demonstrate that all the required sampling, inspecting and testing procedures were actually carried out. Any deviation are fully investigated.
  Releasing or rejecting materials for production use and finished products.
    Batch of product is released for sale or supply prior to certification by a Qualified Person that it is in accordance with agreed product specification
    Rejected materials or products should be handled with care
  Monitoring of all materials, product and environmental conditions in the factory. Sufficient reference samples of starting materials and products are retained to permit future examination of product if necessary and that the product is retained in its final pack unless exceptionally large packs are produced.
Objects of these activities are:
  Starting materials
  Intermediates
  Bulk products
  Finished products
  Environmental conditions

## Slide 13
There shall be QC laboratory attached to each manufacturing unit.
The laboratory shall be capable of performing all the test in accordance to approve specification, or to perform part of test while sub-contracting part of tests to approved contract laboratory.
Where appropriate, QC laboratories shall be separated from production areas especially for microbiology lab.
The laboratories should be designed to suit the operations to be carried out in them. Sufficient space should be given to avoid mix-ups and cross-contamination. There should be adequate suitable space for sample and records.
Separate rooms may be necessary to protect sensitive instruments from vibration, electrical interference, humidity, etc.
QC LABORATORY

## Slide 14
Large firms : Quality Control Unit(s).
Small firms :
  specific tasks unit with limited laboratory apparatus, or
  contract analysis with respective external laboratory institute(s)
Responsibilities defined in written procedures
Independence from production and other departments is fundamental
Under the authority of an appropriately qualified and experienced person
QUALITY CONTROL UNIT

## Slide 15
RESPONSIBILITIES
Examines, approves or rejects incoming materials, intermediates, bulk, the finished products, and returned products.
Does the inspection during production (in-process control)
Establishes, standardizes, and implements all QC procedures, and also establish the specification of each incoming materials.
Establishes specification of intermediates, bulk and finished goods together with head of Production.
Approves reprocessing instruction and rework instruction
Reviews production records to determine errors and ensures that investigations have been conducted and corrective action taken
Involves in all decisions concern with the product quality
Notes: <number>
<footer>
<header>
<date/time>
The head of QC has responsibility as follow:
to approve or reject all the starting materials, an intermediate, bulk, finished products and returned products
to ensure appropriately authorize and dated specification available use
to evaluate batch records
to ensure that all necessary testing is carried out
to approve specifications, sampling instructions, test methods and other Quality Control procedures
to approve and monitor any contract analyst/services
to check the maintenance of his department, premise and equipment
to ensure that the required initial and continuing training of this department personnel is carried out and adapted according to need

## Slide 16
Establishing, verification, and implementing all QC procedures
Evaluating, maintaining, storing, and monitoring all reference standards and retained samples
Reviewing batch documentation
Maintaining correct specification of materials and finished products
Stability testing of each finished product
Participating in :
  complaint investigations
  environmental monitoring
  GMP training
OTHER RESPONSIBILITIES
Notes: <number>
<footer>
<header>
<date/time>
Head of QC shared the following responsibilities with Head of Production on matters relating to Quality:
The authorization of written procedures
The monitoring and control of manufacturing environment
Plant hygiene
GMP training
The approval and monitoring of suppliers of materials
The approval and monitoring of contract manufacturers
The designation and monitoring of storage conditions for materials and products
The retention of records
The monitoring of compliance with GMP requirements
The inspection, investigation, and taking of samples , in order to monitor factor which may affect product quality

## Slide 17
QC DOCUMENTS

## Slide 18
Each specification shall be approved, signed and dated, and maintained by QC unit
The following specification shall be minimally maintained and controlled:
  Starting materials specification
  Process water specification
  Intermediate or bulk product where applicable
  Finished product specification
  Master formula
  Batch Manufacturing Record (BMR)
SPECIFICATION CONTROL

## Slide 19
The following details should be included in the specification:
  designated name, and internal code reference if applicable
  qualitative and quantitative requirement with acceptance limits
Depending on the company practice, other data may be added to the specification:
  the supplier and the original producer
  direction for sampling and testing, or reference to an approved procedure
  storage condition or precautions
  the maximum period of storage before re-examination
STARTING MATERIAL SPECIFICATION

## Slide 20
Drinking water standard is defined as minimum standard for use in cosmetic processing.
  Appropriate specification for chemical and microbial quality should be established based on point of use.
  Periodic testing should be conducted, eg. weekly
Further treatment may be necessary based on the product formula, process and claim requirements. Specification for water with further treatment shall be established based on supplier design specification or pharmacopoeia standard
PROCESS WATER SPECIFICATION
Notes: The company shall carefully reviewed the suitable quality of water to be used. As Water could formed up to 90% of the product content, it is the single most important raw material in many formulas. The choice of water quality will have significant impact on the final product quality and stability.
Baby product or product used near to the eye area, mucus membrane and oral cavity shall use de-ionsed water

## Slide 21
Finished product specification should include:
Designated name, and internal code reference if applicable
Formula number
Description of finished product and its package details
Qualitative and quantitative requirement with acceptance limits
Direction for sampling and testing, or reference to an approved procedure
Storage condition or precautions, if any
Shelf life, if any
Batch numbering requirement (including manufacturing date or expiry date )
FINISHED PRODUCT SPECIFICATION

## Slide 22
Inspection and testing based on process monitoring or actual sample testing at defined sampling interval and location
Shall be documented in Batch Manufacturing Record
The result shall conform to Batch Manufacturing / Packaging Record requirements
Control chart/other statistical tools for process capability may be used for trend analysis
IN-PROCESS CONTROL

## Slide 23
Other laboratory documentation includes
Sampling procedures
Calibration and Maintenance Equipment
Stability Procedures, where applicable
Environment Monitoring, where applicable
Testing procedures and records (including worksheets and/or laboratory notebooks)
Analytical reports and/or certificates
OTHER LABORATORY DOCUMENTATION

## Slide 24
Master Formula and Batch Manufacturing Record shall be retained for the shelf life + 1 year of the product
Other laboratory record (e.g. analytical tests results, environmental controls…) it is recommended that records be kept in a manner permitting trend evaluation
Other raw data such as laboratory notebooks and/or records should be retained and readily available
QUALITY RECORD RETENTION

## Slide 25
TASKS OF
QUALITY CONTROL

## Slide 26
4. Test samples
Meet specification
YES
NO
5. Review of batch record
7. Non conformance or
out of specification investigation
6. Goods release
End
Start
3. Sampling
2. Receiving
8. Goods Reject
End
Lab
Records
Release
QC/QA Status
Quarantine
Reject
Reject
Release
Incoming materials
Water
Returned goods
Intermediates
Bulks
Finished goods
Environment monitoring
Quarantine
QC WORK FLOW

## Slide 27
There should be written procedure on the receiving, internal labeling, quarantine and storage of starting materials, packaging materials and other materials as appropriate
Upon receiving of the supplied goods, its identity, legibility of batch number, integrity of its primary packaging and seal shall be verified prior to acceptance.
Certificate of Analysis shall be provided by the supplier accompanying the receiving of starting materials
Quarantine goods shall be segregated from “Release” goods
Reject goods shall be stored in a define area with consideration of control access (eg. Locked area)
RECEIPT

## Slide 28
The sample taking shall be done in accordance with written procedure that describe:
  The method of sampling
  The sampling tools used
  The amount of samples to be taken
  The type and condition of the sample container to be used (ie amber glass bottle)
  The identification of the container sampled
  Special precaution for hazardous materials
  The storage condition (if any)
  Instruction for cleaning and storage of sampling equipment
  Instruction for re-sealing the opened container.
SAMPLING

## Slide 29
SAMPLING PROCESS
Sampling tools such as knives, pliers, saws, hammers, wrenches, implements to remove dust (preferably a vacuum cleaner)
Material to re-close the packages (such as sealing tape), as well as self-adhesive labels to indicate that a part of the contents has been removed from a package or container.
Containers due to be sampled should be cleaned prior to sampling if necessary.
There should be a written procedure describing the sampling operation. This should include health and safety aspects of sampling.
The container used to store a sample should not interact with the sampled material nor allow contamination. It should also protect the sample from light, air, moisture, etc., as required by the storage directions for the material sampled.
Microbiology sampling tools shall be sterilised prior to use
Aseptic technique shall be used during sampling

## Slide 30
Raw Material
Sampling plan for raw material should be based on defined sampling standard, for example:
  the “n plan” is based on the formula n = 1+√N, where N is the number of sampling units in the consignment;
  the “p plan” is based on the formula p = 0.4 √N, where N is the number of sampling unit; or
  the “r plan” on the formula r = 1.5√N .
  reduce sampling plan such as “p plan” shall be considered only when there is established confidence on the material’s uniformity.
Packaging materials and Finished Product
Sampling plans for packaging materials should be based on defined sampling standards, for example British Standard BS 6001-1, ISO 2859 or ANSI/ASQCZ1.4-1993.
SAMPLING PLAN

## Slide 31
Scoop for solid
Dip tube for liquid
Weighted container for large tank
Spears for bag
SAMPLING TOOLS

## Slide 32
TESTING & ANALYSIS
All tests shall be performed in accordance with the test methods as stated in the specification
Reduce testing rational shall be documented
Test can be performed by in-house laboratory or external laboratory
Where test is performed in-house, laboratory shall be available

## Slide 33
LABORATORY DATA (1)
QC should maintain adequate analytical records concerning the examination of materials and products.
Such records should include among others:
  The result of every test performed, including observations and calculations, relating to compliance with the established specifications (calculations done on scratch paper shall be included in the record).
  The source of the specification used.
  Signature(s) of the person(s) who performed the quality control procedure.
  A final review (eg. laboratory management), the decision taken, and a dated endorsement by a duly authorized expert (eg. supervisor/manager).
Notes: Peer review for the laboratory record is acceptable practice

## Slide 34
LABORATORY DATA (2)
Laboratory data must be recorded in a manner that assures its accuracy, authenticity and completeness, preserves its integrity and assures its retrievability
Data recording should be clear, permanent (not pencil) and traceable to the item tested.
Records, either handwritten or equipment/ computer generated, shall be reviewed, signed off and dated.
There should be a written policy about averaging of numbers, cross-outs of mistakes, significant figures, leaving notebook pages or fill-in-the-blank entries empty, etc.

## Slide 35
RETAIN SAMPLE (1)
Retain sample should be representative of the batch of materials or products from which they are taken.
Retain sample shall be of a size sufficient to permit at least 2 full re-examinations
Retain samples for each batch of finished products shall be retained at a defined period
Finished product should be kept in their final packaging and stored under the recommended condition (eg. Consumer use condition at room temperature)

## Slide 36
RETAIN SAMPLE (2)
A retain sample log shall be maintained with the sample identification, batch number and its storage location for ease of retrieval
Prior to disposal of retain sample, visual inspection should be carried out

## Slide 37
CONTROL OF
STARTING MATERIAL ACCEPTANCE
All starting materials shall be verified prior to use.
Verification should include the following:
  Review of Certificate of Analysis from the manufacturer versus approved specification
  Other tests may be conducted as appropriate:-
    Identification test / package identification and other characteristic of the material shall be examined.
    Primary packaging: No leakage, sharp dents, tear , exposed parts and seal integrity
    Legible label and identification and batch number
  Frequency: Every batch of manufacturer’s batch

## Slide 38
CONTROL OF
PROCESS WATER ACCEPTANCE
Minimally meet National or WHO Drinking Water standard.
Treated water specification shall be based on supplier’s design specification or pharmacopoeia standard

## Slide 39
CONTROL OF
IN-PROCESS BULK/PRODUCT ACCEPTANCE
In-process inspection and testing should be performed by monitoring the process or by actual sample analysis at defined locations and time.
The results should conform to established process parameters or acceptable tolerances.
Line clearance shall be practiced on all packaging lines
Where necessary, standard reference for labeling and coding format/ requirement should be available.

## Slide 40
CONTROL OF
FINISHED PRODUCT ACCEPTANCE
Review of Batch Manufacturing Record
Review all non-conformance or deviation documented on the BMR and its reprocessing or rework instruction
Review of physical, chemical and microbiological results
Review of sample from the batch for verification on its conformance to BMR requirement.
Approve Certificate of Analysis with clear summary statement on the product status, ie “Release” or “Reject”

## Slide 41
OUT OF SPECIFICATION INVESTIGATION
Written procedure should be made available.
Typically, an investigation includes:
  A review of the calculation to ensure they are correct.
  A review of test procedures utilized.
  A review of equipment, columns, charts and previous analyses of samples of the same product/material
  A review of reagent/ standardization carried out for the test (e.g., pipettes).
  A complete investigation and evaluation of initial results prior to a retest.
  A review of product/material history
  Assigned person responsible for investigation
  Documented rational for retest and re-sampling
Proper documentation of investigations, recommendation and disposition must be in place.

## Slide 42
LABORATORY REAGENT
Reagent should be prepared in accordance with written procedures.
Volumetric solution, the last date of standardization and the last current factor should be indicated.
Where necessary, the date of receipt of any reagents should be indicated on the container. Instruction for use and storage should be followed.
Where necessary, the identification test and/or other testing of reagent materials is required upon receipt or before use.
Reagent to be certified by the original producer to the quality of reagent grade purchased, typically a CoA shall be available for review and verification on acceptance.
Laboratory safety manual shall be available for safe operation of the reagent and chemicals.

## Slide 43
LABORATORY REAGENTS
All reagents should bear a label containing the following information :
  The name of the reagent
  Its strength or concentration
  Its expiration date
  Date of preparation
  Name of the individual who prepared it
  Material Safety Data Sheet (MSDS)

## Slide 44
ENVIRONMENT MONITORING (1)
Environment Monitoring to be implemented where appropriate.
The objective is to demonstrate the manufacturing environment is functioning at an adequate level of microbial control for the specific product/product group.
Sample site selection based on:
  Room design/ size
  Manufacturing process
  Product susceptibility
Potential sampling site shall include
  Starting material sampling room/area
  Dispensing area
  Manufacturing area
  Microbiological lab
Notes: Where appropriate refer to the critical manufacturing area, it is important to ensure the environment monitoring is carried out to ensure effectiveness of the cleaning and sanitation program

## Slide 45
ENVIRONMENT MONITORING (2)
Alert and Action limits should be established based on statistical methods.
Sampling frequency shall be established, eg weekly.
The media selection for use of detection and growth of viable airborne particulate shall be established.
Direct and in-direct methods available, most commonly used are STA air sampler, SAS air sampler and settling plate.
Notes: STA (Slit-to-Agar) Air Sampler: Uses a revolving agar plate at a precise distance from a slit type orifice to impinge the air sample (and particulate) directly onto the surface of a solid nutrient collection medium
Surface Air Sampler (SAS): Air is drawn into the unit by means of an impeller, is drawn over the surface of a contact plate and is exhausted.

## Slide 46
STABILITY STUDY (1)
Stability test shall be carried out where applicable
Real time stability shall extend to the end of shelf life period for any new products and should include the following parameters:-
  Number of batch(es) for different batch size
  Relevant physical, chemical, microbiological test methods
  Acceptance criteria
  Description of the container closure system(s)
  Testing intervals (time points)
  Description of the condition of storage

## Slide 47
STABILITY STUDY (2)
The number of batches and frequency of testing shall provide a sufficient amount of data to allow for trend analysis.
Bracketing and matrixing design may be applied where applicable.
Worst case situation shall be covered within the real time stability program after any significant change or deviation to the process or package, ie. After rework or reprocessing.
A summary of data should be generated, with interim conclusion on the trend analysis.
Result of stability studies should be reviewed by authorized person(s).

## Slide 48
CALIBRATION
To maintain the accuracy and precision of test equipment at all times.
To ensure highest level of confidence in all measurement that affect materials disposition decision, with unbroken chain of traceability to national standard.
To determine whether the equipment is still fit for its intended purpose.
It is based on the comparison of a primary standard or instrument of known accuracy with another equipment (to be calibrated)
It is used to detect, correlate, report or eliminate by adjustment of any variation in the accuracy of the equipment being calibrated.

## Slide 49
EQUIPMENT CLASSIFICATION
Critical equipment:
  Direct measurement that affect the final product quality
  Measurement on critical process parameters in the process specification
Non critical equipment:
  Indirect measurement that will not directly affect the final product quality
  Shall be maintained based on company maintenance schedule

## Slide 50
CALIBRATION INTERVAL
Depending on:
  Classification of Critical or non-critical
  Usage (light or heavy usage)
  Handling (light or heavy handling)
  Manufacturer’s recommendation
  Reference to NIST or accreditation body guideline for a specific measurement system

## Slide 51
PRIMARY STANDARD
Highest accuracy order in the measurement system
Traceable to National or International standard

## Slide 52
Note: * Working Standards
REFERENCE STANDARD*/MATERIAL
Reference Standard
It shall be calibrated by a body that can provide traceability. Such reference standard of measurement held by the laboratory shall be used for calibration only. It shall be calibrated before and after any adjustment
Reference Materials
Where possible, it shall be traceable to SI units of measurement, or to Certified Reference Materials. Internal Reference Material shall be checked as far as is technically and economically practical

## Slide 53
CALIBRATION RESULT
Traceable to National or International standard
Measurement standard to be specified with validity period
Conclusion made on the validity of calibration
Certificate to be reviewed by authorize personnel

## Slide 54
VERIFICATION
Applicable to equipment that cannot be calibrated (adjustment, correlation, etc)
Verification against measurement standard with correction factor documented
Actual reporting of result shall include the correction factor
Temperature correction factor “- 2 0C”.
  Measured value: 240 C
  Reported value = 24 0 C –2 0 C= 22 0 C

## Slide 55
OUT OF CALIBRATION
Remove equipment from use
Out of Calibration Investigation to be carried out to determine the source of inaccuracy
Evaluate the impact of OOC result on the final product quality and other previously measured data
All investigation findings should be documented

## Slide 56
CALIBRATION RECORDS
Calibration Master Plan
Include the control of all critical measurement equipment that contain the following details
  Name
  Identification by model # and serial #
  Location
  Owner/Responsible
  Calibration Frequency
  Calibration due date
Calibration Certificate
Calibration Procedure

## Slide 57
CALIBRATION CERTIFICATE
Name and address of contracted calibration laboratory
Name and address of client
Description and identification of item calibrated
Environment conditions when calibration was made
Date of receipt of instrument, date of calibration and date of next calibration
Calibration method
Result of calibration
Signature and title of person responsible for the calibration
External calibration contract shall be awarded to Accredited by the nation institution

## Slide 58
CALIBRATION IDENTIFICATION
Status of equipment calibration shall be available and affixed to the equipment where applicable.
Equipment identification shall bear the following information:
  name of equipment
  serial no.
  date calibrated
  status
  schedule of next calibration and
  initial/signature of the person who performed the calibration

## Slide 59
REPROCESSING (1)
Reprocessing includes both definitions of Reprocessing and Rework
Definitions
  Reprocessing: Subjecting all or part of the batch/lot of an in-process bulk, intermediate or product of a single batch or lot to the previous step of the approved manufacturing/packaging process due to failure to meet pre-determined specification.
  Rework: Subjecting all or part of the batch /lot of an in-process bulk, intermediate or product of a single batch or lot to an alternate manufacturing/ packaging process due to failure to meet pre-determined specification.
Notes: QC personnel must have access to production areas for, for example, sampling and inspection. However, this must be balanced because it may not be appropriate, for instance, to have QC staff enter aseptic filling suites, or areas where there is highly potent dangerous material

## Slide 60
Complete OOS/Non-conformance investigation with risk assessment on recovery decision, based on approved procedure
Reprocessing Instruction includes the following details:
  Additional Ingredient where necessary
  Reprocessing instruction
  Responsibility
  Sampling Plan
  Acceptance Criteria
Approval of Reprocessing Instruction by QC
Where batch adjustment which is part of the In-Process Quality Control, this should not be considered where there is reprocessing.
REPROCESSING (2)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61
CONTROL OF
REPROCESSING PRODUCT
Meeting the Reprocessing Instruction acceptance criteria
Where the stability of the product is in doubt, additional testing of any finished product which has been reprocessed should be performed, stability study to be included as appropriate.
Notes: <number>
<footer>
<header>
<date/time>
QC personnel must have access to production areas for, for example, sampling and inspection. However, this must be balanced because it may not be appropriate, for instance, to have QC staff enter aseptic filling suites, or areas where there is highly potent dangerous material such as oncology (or cytotoxic material) or anovulent hormones.

## Slide 62
RETURN (1)
Definition- Finished product that has been distributed and is being returned for reasons other than a product complaint reason.
Returned products shall be identified as such and put on hold. If the conditions under which returned products have been held, stored, or shipped before or during their return, or if the condition of the product, its container, carton, or labeling, as a result of storage or shipping, casts doubt on the safety, identity or quality of the product, the returned product shall be destroyed unless examination, testing, or other investigations prove the product meets appropriate standards of safety, identity or quality.

## Slide 63
A product may be reworked/reprocessed provided the subsequent product meets appropriate standards, specifications, and characteristics.
Records of returned products shall be maintained and shall include the name, lot number (or control number or batch number), reason for the return, quantity returned, date of disposition, and ultimate disposition of the returned product.
RETURN (2)

## Slide 64
RETURN (3)
If the reason for a product being returned implicates associated batches, an appropriate investigation shall be conducted.
Procedures for the holding, testing, and reprocessing of returned products shall be in writing and shall be followed.
The recovery rational shall be documented with approval from the QC unit.
Disposal of return goods shall be based on approved procedure.

## Slide 65
CONTROL OF RETURN PRODUCTS
Products that have been subjected to improper storage conditions including extremes in temperature, humidity, smoke, fumes, pressure, age, or radiation due to natural disasters, fires, accidents, or equipment failures shall not be salvaged and returned to the marketplace.
Whenever there is a question whether products have been subjected to such conditions, salvaging operations may be conducted only if the following acceptance criteria were fulfilled:
  Product labeling meeting current regulatory requirements
  Laboratory tests that the product meet the product specification
  Visual inspection on the product and their associated packaging were intact and comparable to standard

## Slide 66
Trainer Manual of GMP ASEAN Quality Control
ASEAN GMP Supplementary Module : Water
ASEAN GMP Supplementary Module : Calibration
WI of QC Working Procedure
WI of Sampling of Incoming Raw Materials
WI of Sampling of Incoming Packaging Materials
WI of Handling Incoming Materials
WI of Handling Finished Goods
WI of Handling and Testing of Raw Materials
WI of Stability Study
WI of Environment Monitoring
RELATED HYPERLINK DOCUMENTS

## Slide 67
REFERENCES
Guideline on ASEAN Cosmetic GMP (2003)
U.S. Food Drug Administration, Center for Food Safety Applied Nutrition, Cosmetic Compliance program
NIST
WHO Guideline for Drinking Water Quality
EUDRALEX, Medicinal Products for Human and Veterinary Use : Good Manufacturing Practice, ,Volume 4.
WHO, Good Manufacturing Practices: Starting Materials.
Ariffin F., Consultation to Discuss : Stability Studies in a Global Environment.
International Pharmacopoeia
WHO Guideline For Sampling OF Pharmaceuticals and related materials.
PDA Technical Report No. 13 revised, Fundamentals of an Environmental Monitoring Program
Notes: <number>
<footer>
<header>
<date/time>
Definition
QC Overview
Scope
General Principles
Responsibility
Quality Control Laboratory
Specification Control
In-Process Quality Control
Laboratory Documentation and Retention
Starting Materials and Packaging
Receipt
Sampling
Testing
Control of Starting/Packaging Materials Acceptance
Control of Process Water Acceptance
Control of Finished Product Acceptance
Out of Specification Investigation
Laboratory Reagent
Environment Monitoring
Stability Study
Calibration
Sub-contracting of Test and Calibration
Reprocessing
Return
Reference

## Slide 68
Thank You