## Slide 1: SUPPLEMENTARY ASEAN GMP TRAINING MODULE EQUIPMENT SANITATION
Prepared by :
Ofelia M. Malagkit - Philippines
Approved by
ASEAN Cosmetic GMP Team
Endorsed by
ASEAN Cosmetic Committee

## Slide 2
EQUIPEMNT
SANITATION

## Slide 3
The main principle for equipments should be that it is easy to dismantle or remove to facilitate cleaning by non-corrosive materials.
Design, type, size and installation of equipment shall be in such a way that avaoid and prevent any contamination during manufacturing
When choosing and buying machines, hygienic production and possibilities for cleaning and disinfection must be considered.
Contamination is a leading cause of machinery failure. Maintenance and reliability professionals need to comprehend the destructive nature of contamination and realize the benefits in removing contamination from their facilities.
SANITATION PRINCIPLES
Notes: Principles of equipment sanitation :
The main principle for equipments should be that it is easy to dismantle or remove to facilitate cleaning and that it should be made of non-corrosive materials.
Design, type, size and installation of equipment shall be in such a way that any contamination that might occur during manufacturing such as lubricants, dust, metals is prevented, avoided and minimized
Cleaning and disinfection will often be complicated or impossible because of the complex construction of machines and when choosing and buying machines, hygienic production and possibilities for cleaning and disinfection must be considered.
Contamination is a leading cause of machinery failure. Maintenance and reliability professionals need to comprehend the destructive nature of contamination and realize the benefits in removing contamination from their facilities. If foreign materials enter your system, critical responses are necessary to minimize the effects of destructive contaminants.

## Slide 4
Cleaning operations shall be performed in a manner to prevent contamination of materials and products.
Only cleaning compounds and sanitizers authorized for product contact surfaces shall be used for cleaning.
When not in use, all cleaning compounds and sanitizers shall be properly labeled and stored in a locked compartment, away from production and food storage areas.
Cleaning equipment and tools shall be supplied and be readily available for use
Equipment and utensils should be kept clean.
The written instruction for cleaning and sanitation for each equipments and utensils should be provided.
CLEANING PRACTICES
Notes: Cleaning practices :
Cleaning operations shall be performed in a manner to prevent contamination of materials and products. Cleaning methods shall be done in a manner to minimize the potential for product contamination.
Only cleaning compounds and sanitizers authorized for product contact surfaces shall be used for cleaning. Appropriate verification procedures or testing shall be done periodically to insure that the concentration of Clean-In-Place (CIP) and other cleaning chemicals are consistent with the product labeling.
When not in use, all cleaning compounds and sanitizers shall be properly labeled and stored in a locked compartment, away from production and food storage areas..
Cleaning equipment and tools shall be supplied and be readily available for use. All cleaning equipment shall be maintained and stored in such a way as not to contaminate foods or food equipment.
Equipment and utensils should be kept clean
  Vacuum or wet cleaning methods are preferred. Compressed air and brushes should be used with care and avoided if possible as they increase the risk of product contamination
  Standard operating procedures must be followed for cleaning and sanitizing of major machines
Cleaning and sanitization procedures :
  shall be validated as to its
  effectiveness in removing contaminants and residues.

## Slide 5
Written SOP’s shall be established specifying:
areas, equipment to be cleaned
cleaning and sanitization procedure for each area, equipment
cleaning and sanitization frequency such as between individual batches, change over from one product to another, plant shutdown or new equipment
precautions to minimize contamination and spread or microorganisms
personnel assigned to do the cleaning
<number>
CLEANING PROCEDURE
Notes: Guidance for work instruction for cleaning procedure is attached in hyperlink documents

## Slide 6
1. Foam: Foam is produced through the introduction of air into a detergent solution as it is sprayed onto the surface to be cleaned. Foam cleaning will increase the contact time of the chemical solutions, allowing for improved cleaning with less mechanical force and temperature.
2. High Pressure: High pressure cleaning is used to increase the mechanical force, aiding in soil removal. In high pressure cleaning chemical detergents are often used along with increased temperature to make soil removal more effective.
3. Clean in Place (CIP): CIP cleaning is utilized to clean interior surfaces of tanks and pipelines of liquid process equipment. A chemical solution is circulated through a circuit of tanks and or lines then returned to a central reservoir allowing for reuse of the chemical solution. Time, temperature, and mechanical force are manipulated to achieve maximum cleaning.
4. Clean Out Of Place (COP): COP cleaning is utilized to clean tear down parts of fillers and parts of other equipment which require disassembly for proper cleaning. Parts removed for cleaning are placed in a circulation tank and cleaned using a heated chemical solution and agitation.
5. Mechanical: Mechanical cleaning normally involves the use of a brush either by hand or a machine such as a floor scrubber. Mechanical cleaning uses friction for food soil removal.
<number>
CLEANING METHOD

## Slide 7
FACTOR INFLUENCE CLEANING
There are 4 interrelated factors which effect the overall cleaning process.
When designing cleaning procedures these factors need to be carefully considered:
  Cleaning time
  Temperature
  Chemical being used
  Mechanical forces
Notes: There are 4 interrelated factors which effect the overall cleaning process. When designing cleaning procedures these factors need to be carefully considered.
Time: The longer a cleaning solution remains in contact with the equipment surface, the greater the amount of dirt that is removed. Increasing time reduces the chemical concentration requirements.
Temperature: Dirt are affected to varying degrees by temperature. In the presence of a cleaning solution most dirt become more readily soluble as the temperature is increased.
Chemical Concentrations: Chemical concentrations vary depending upon the chemical itself, type of dirtl, and the equipment to be cleaned. Concentration will normally be reduced as time and temperature are increased.
Mechanical Force: Mechanical force can be simple hand scrubbing with a brush or as complex as turbulent flow and pressure inside a pipeline. Mechanical force aids in dirt removal and typically reduces time, temperature, and concentration requirements.

## Slide 8
FUNDAMENTAL CLEANING PROCESS
The following is the typical procedure used when cleaning processing equipment:
  The factors that influence cleaning (time, temperature, chemical concentration, and mechanical force),
  the method of cleaning,
  and the dirt type to be removed will ultimately determine the cleaning procedures selected for use.
Notes: The following is the typical procedure used when cleaning processing equipment, such as
The factors that influence cleaning (time, temperature, chemical concentration, and mechanical force),
the method of cleaning, and
the dirt type to be removed will ultimately determine the cleaning procedures selected for use.
Several guidance for cleaning process:
Clearance for cleaning: It is recommended that each person in processing be responsible for clearing the area concerned as this tends to intensify discipline regarding tidiness and hygiene. The purpose of clearance after work is to prepare an easy and quick cleaning procedure. Clearance implies removal of all items which may retard performance.
Pre-Rinse: Dirty equipment surfaces are rinsed with warm water to remove the gross amounts of loose dirt.
Cleaning Cycle: Removal of residual product from equipment surfaces through manipulation of the four basic cleaning factors and the method of cleaning. Typically alkaline chemical solutions are used for the cleaning cycle.
Rinse: Rinsing of all surfaces with cold to hot water, depending upon the temperature of the cleaning cycle, to thoroughly remove all remaining chemical solution and product residues.
Acid Rinse: A mild acid rinse of the equipment neutralizes any alkaline residues left and removes any mineral dirt present.
Sanitize: All equipment surfaces are rinsed or flooded with a sanitizing agent. Time and concentration are critical for optimum results.

## Slide 9
There are two classes of cleaning compounds :
  acid cleaners, and
  alkaline cleaners.
Chemical formulations for acid and alkaline compounds vary widely providing for selection flexibility when considering sanitation procedures, such as :
  types of processing equipment to be cleaned,
  chemical dispensing, and
  method of cleaning.
<number>
CLEANING COMPOUNDS
Notes: Cleaning coumpound description :
There are two classes of cleaning compounds, acid and alkaline.
Chemical formulations for acid and alkaline compounds vary widely providing for selection flexibility when considering sanitation procedures, types of processing equipment to be cleaned, chemical dispensing, and method of cleaning.
Acid cleaners :
  Phosphoric Acid: Phosphoric acid provides the bulk of the acidity in most acid cleaners. Phosphoric solublizes minerals well and is less corrosive to metals than most other acids.
  Other Acidulants: Acetic, hydroxyacetic, citric, sulfamic, and nitric acids are also used in many cleaners to a varying degree. Nitric acid use has expanded greatly due mainly to cost, however nitric is very effective in the removal of tough mineral deposits in heat exchangers and evaporators.
  Surface Active Agents (Surfactants): Surfactants help break down the surface tension of soils to improve removal. Once the food soil is removed the surfactant forms a colloidal suspension with the soil, keeping it water soluble to prevent it from redepositing on the equipment surfaces.
Alkaline cleaners :
  Sodium or Potassium Hydroxide: Hydroxides provide the largest portion of alkalinity and effectively saponify fats and peptize proteins for removal
  Sodium Metasilicate: Aids in emulsifying and soil suspension along with protecting against metal corrosion.
  Complex Phosphates: Phosphates primary function is to soften the water by chelating (binding up) the calcium and magnesium hardness. This allows for better cleaning effectiveness and reduces mineral deposits. Phosphates will also aid in emulsifying food soils.
  Surface Active Agents (Surfactants): Surfactants help break down the surface tension of soils to improve removal. Once the food soil is removed the surfactant forms a colloidal suspension with the soil, keeping it water soluble to prevent it from redepositing on the equipment surfaces.
  Chlorine: Chlorine is added to many chemical formulations to help in peptizing proteins.

## Slide 10
<number>
Cleaning and sanitization records/log books must be kept in all manufacturing areas in which the operator shall record the area, equipment cleaned and sanitized, sign the record to be countersigned by another individual who checks the cleanliness
sanitation of the equipment.
CLEANING RECORD

## Slide 11
The main objective of a cleaning programme is to control microbial activity. Although an adequate cleaning programme will eliminate nearly all the soil present, it will not destroy or remove all the microorganisms.
This requires a second step “sanitation”
Sanitation methods can be divided into two groups:
1. Non-chemical disinfection methods
2. Chemical disinfection methods
SANITATION PRINCIPLES
Notes: Sanitation methods :
Non chemical method
  In many cases hot water (900 C or more) or steam is the best way for sanitation purpose, but it may be inconvenient or impractical due to the following reasons :
    Providing hot water or steam is expensive and may cause materials to deteriorate and equipment to distort.
    If steam is used it will take considerable time to heat and cool equipment. It may cause baking-on product and other residues.
    Visibility is reduced in the environment thus reducing the effectiveness of the sanitizing procedures.
    Finally it gives condensation problems.
  Insufficient heating may result in the incubation of microorganisms in inaccessible parts of the machines and the equipment.
Chemical method
  The most essential for an effective chemical sanitation program is a clean surface. Consequently, to achieve microbial control the cleaning and sanitation program must be thorough, compatible and totally effective.
  The choice of chemical disinfectants is determined by the following considerations:
    Public health regulations
    Spectrum of effectiveness, i.e. ability to kill many types of microorganisms
    Must be efficient under the conditions of use
    Quick action
    Presence or absence of organic matter
    Corrosive properties
    Type of processing area and type of surface to be disinfected
    Non-toxic and gentle to the skin
    Inexpensive
    Must not affect the odour or flavour of the product on the equipment
    Must be easily rinsed away and leave no toxic residues
    Easy to dispense and to handle
    Must be safe in use and must not affect the operators who use it.
  Manufacturers offer a large number of disinfectants, each claimed to be the best on the market. Nevertheless the only ones suitable for the cosmetic industry contain chemicals of one of the following groups:
    Chlorine and chlorine-releasing compounds
    Quarternary ammonium compounds
    Amphoteric (ampholytic) compounds
    Phenolic compounds
    Peracetic acid

## Slide 12
<number>
CLONCLUSION
Proper cleaning and sanitation process of each equipment can avoid :
cross contamination
mix-up

## Slide 13
<number>
ASEAN Guideline for Cosmetic GMP, 2003
WHO Basic Principle of GMP : Sanitation & Hygiene, 2000
Bishop, Basic Principle of Sanitation, N.E.M. Business Solutions, 1997
Health Services Agency, County of Santa Cruz, Cross Contamination, 1999
www.maintenanceconference.com
REFERENCES

## Slide 14
Thank You