## Slide 1: ASEAN GMP TRAINING MODULE DOCUMENTATION
Prepared by
Hardaningsih - Indonesia
Nguyen Van Loi - Vietnam
Approved by
ASEAN Cosmetic GMP Team
Endorsed by
ASEAN Cosmetic Committee
Notes: This module deals with the very important topic of documentation.
It is a half to one-day training session (depending on the participants ability and experience) divided into 2 roughly equal parts:
  In each half, there will be 45 - 60 minutes of presentation,
  60 minutes discussion in groups and 30 minutes feedback to the whole group.
There will be one test and discussion (40 minutes) covering the whole module that will be taken at the end.

## Slide 2
Introduction
  Objective
  Purpose of documentation
Quality System Documentation
  Tiers of documentation
  Quality Manual
  Quality Procedures
  Work Instructions
  Quality records
Format of documents
How to create good documentation system
Manufacturing documents
References
CONTENT OF PRESENTATION

## Slide 3
INTRODUCTION

## Slide 4
INTRODUCTION
A reliable evidence for GMP compliance.
Quality by design is the only solution to overcome the quality-related complaints in an organisation.
An essential element of quality assurance is good documentation practices.
The system of documentation devised or adopted should have as its main objective to establish, monitor, and record “quality” for all aspects of the production, quality control and quality assurance

## Slide 5
OBJECTIVES
To review general requirements for documents
To review specific requirements for each document
To give general guidance how to create good documentation system
Notes: <number>
<footer>
<header>
<date/time>
There are three objectives for this session:
1. We are going to start by looking at the general requirements for all documents and to review the types of documents listed in the ASEAN GMP text.
2. Then we will look at the specific requirements for each type of document.
3. Finally, we will look at the specific issues how to create and write good documentation system that meet GMP requirements

## Slide 6
PURPOSE
Clearly written documentation prevents errors that may arise in oral or casually written communication
It provides assurance that quality related activities are carried out exactly the way they have been planned and approved
The achievement of conformity and quality improvement
Purpose of documentation :
  To ensure that there are specifications for all materials and methods of manufacture and control
  Employees know what to do
  Responsibilities and authorities are identified
  Ensure that authorized persons have all information necessary for release
  Provide audit trail
  Forms the basis for improvement.
Notes: <number>
<footer>
<header>
<date/time>
Documentation is an essential part of quality assurance and relates to all aspects of GMP.
The cosmetic industry must have a good document framework (infrastructure).
It is important for a manufacturer to get the documentation right in order to get the product right.
There are a number of purposes for documents:
  They are used to define specifications for materials and for methods of manufacture and control.
  They ensure that everyone concerned with manufacture and QC knows what to do, how and when to do it.
  They allow decisions to be taken on batch release.
  They provide an audit trail, which is particularly important in the case of suspect batches. Write what you do, do what you write and if you didn't write what you did...you didn't do it!!

## Slide 7
QUALITY SYSTEM
DOCUMENTATION

## Slide 8
QUALITY SYSTEM DOCUMENTATION
Documentation is the key to operating a cosmetic company in compliance with GMP requirements.
All the elements, requirements and provisions adopted by cosmetic company for its quality system should be documented in a systematic, orderly and understandable manner in the form of policies and procedures.
Documents should be designed, prepared; reviewed and distributed with care.
It should be written in detail and in simple language that can be understood by the user.

## Slide 9
Broadly, all documents relating to quality fall in to the following categories:
  Quality Manual
  Quality Procedures
  Supporting Documents or Work Instructions
  Quality Records
All levels are integrated to form a comprehensive and cohesive documentation network via a system of cross referencing
Quality Records
Supporting Documents or Work Instructions
Quality Procedures
Quality Manual
TIERS OF DOCUMENTATION

## Slide 10
QSP #03
QSP #02
QUALITY
STANDARD PROCEDURE
QSP #01
QUALITY
MANUAL
QM
TIERS OF DOCUMENTATION
WI #03
WI #02
WORK
INSTRUCTION
WI #01
WP #03
WP #02
WORK
PROTOCOL
WP #01
STD #03
STD #02
STANDARD TEST /
SPECIFICA-TION
STD #01
CE #03
CE #02
CODE
ETHICS /
WORK
POLICY
CE #01
IL #03
IL #02
IDENTITY
LABELS
IL #01

## Slide 11
The strategic document that outlines the organization’s system of providing quality assurance to achieve customer satisfaction.
Objectives :
Describe the quality system structure
Declare the quality policy and organization goal
Describe how the organization meets the quality goal
QUALITY MANUAL
Quality Records
Supporting Documents or Work Instructions
Quality Procedures
Quality Manual
Content of quality manual :
The quality policy declaration
The goal of quality;
The organisational structure including responsibility and authority of each key personnel
Procedures, instructions and resources for implementing the quality management.
User :
All personnel in the organization
Another parties, auditors, and customers
Notes: <number>
<footer>
<header>
<date/time>
The Quality Manual could be in one document supported by several tiers of document, each becoming progressively more detailed.

## Slide 12
The tactical document that outlines the activities or operations of the organization in implementing the stated quality policies.
QUALITY STANDARD PROCEDURES
Quality Records
Supporting Documents or Work Instructions
Quality Procedures
Quality Manual
Objectives :
Describe detail explanation how activities should be done, controlled and recorded in implementing the definite policy
Standard Operation Procedures explains:
What the process is and it’s purpose
Where activity is operating
Who is responsible for every activity
When activity is completed, sequential of the activities, frequency, etc.
How activity can be finished follow the work instruction design or other reference documents
Reference to the other relevant documents
User :
All personnel who set up and run the processes

## Slide 13
The operational document containing instructions specifying how the activities are performed or products are accepted.
WORK INSTRUCTIONS
Quality Records
Supporting Documents or Work Instructions
Quality Procedures
Quality Manual
Objectives :
It is an instruction document, step by step for guideline to execute the daily activity or operation for personnel in every function
It is used departmentally, every task or every line.
Content of work instructions :
Detailed explanation of instructions to finish the job, detailed handling of method, equipment and machine
Related to the technical matters with stressing for operation, inspection & testing.
User :
All personnel who operates the certain task
Format :
Worksheet, sample, checklist
Audiovisual (tape, video,illustration, photo)

## Slide 14
S.O.P. versus W.I.
Process oriented
Describe step of procedure
Supporting the Quality Manual
Explain general description on certain process and give systematic action to ensure product quality
Procedure guideline which involve several departments and/or sections
During implementation need other supported documents
Guideline at organization level
QUALITY PROCEDURE/SOP
Task oriented
Describe detail instruction
Operation guidance
Dedicated to explain special task, method, or technique which should be done to achieve target quality
Instruction guidance which dedicated for certain department or section only
During implementation can stand alone
Guidance at operational level
WORKING INSTRUCTION

## Slide 15
Quality Records, including charts and data pertaining to design, inspection, testing, survey, audit, review or related results, should be maintained as important evidence to demonstrate:
effectively of Quality System Implementation;
that products and services have been developed and delivered appropriately with the requirements.
All Quality Records should be :
legible and clear;
Dated;
readily identifiable and retrievable;
carry authorization status;
retained for a designated period;
protected from damage and deterioration while storage.
QUALITY RECORDS
Quality Records
Supporting Documents or Work Instructions
Quality Procedures
Quality Manual

## Slide 16
FORMAT OF DOCUMENT

## Slide 17
FORMAT OF DOCUMENT
No “best format” in documentation system.
Each document should be suitable for all users
In general, all quality documents can be written in the following format :
  narrative
  flowchart
  combination narrative and flowchart
  electronic / computerized system

## Slide 18
NARRATIVES DOCUMENT
The most common format being used
The narrative document can be described as the following :
  Policy reference
  Objective : why and for what
  Coverage area
  Document reference
  Responsible person
  Detail procedure
  Record if needed

## Slide 19
FLOWCHART DOCUMENT
Schematic representation which describe the flow of processes in certain target activity
Very clear and easy to read
Sample of the flowchart document can be written as beside schema

## Slide 20
Basic Flowchart Languages
FLOWCHART

## Slide 21
Sometimes narrative document & flowchart is supported by design / lay out
Legend
= Mixer
= Intermediate bin with activated discharge
= Feed metering unit
= Metal separator
= UPZ fine impact mill with pin discs
= UPZ fine impact mill with pin discs
= Automatic reverse-jet filter
= Fan
= Rotary valve
= End-product bin with activated discharge
= Bagging unit
= Control cabinet
A = Feed product
B = Perfume addition
C = End product
COMBINATION DOCUMENT

## Slide 22
ELECTRONIC DOCUMENT
Geared towards assuring data integrity of computerized systems used to meet predicted rule requirements
Using ERES (Electronic Records; Electronic Signatures)
Detail ERES can be found at the attached document
Notes: <number>
<footer>
<header>
<date/time>
Some documents may be stored electronically. Special controls have to be developed. If documentation is handled by electronic data-processing methods, only authorized persons should be able to enter or modify data in the computer, and there should be a record of changes and deletions; access should be restricted by passwords or other means, and the entry of critical data should be independently checked. Whichever way the master is stored, it is important that clear copies are reproduced for use with individual batches.

## Slide 23
HOW TO CREATE
GOOD DOCUMENTATION SYSTEM

## Slide 24
Document is :
  complete history of each batch
  from starting materials to finished products
  record activities for :
    maintenance
    storage
    quality control
    primary distribution
    specific matter related to GMP
Documents should be designed, prepared, reviewed and distributed with care
All documentation must be organized into files which must be maintained for specified periods of time after the expiry date of the product.
DOCUMENT
Notes: <number>
<footer>
<header>
<date/time>
In terms of design, there is no single right answer – the one thing you can be sure about is that every company will come up with a different design. However, it is better for the operators if a consistent approach is taken.
It is possible for some of the documents to be combined, but generally they should be separate.
Documents should be designed, prepared, reviewed and distributed with care.
All documents should :
Legal evidence
Permanent record
Clear
Legible
Complete
Accurate
Real-time records
Consistent
Records events sequentially
Reviewed and approved by those responsible and accountable

## Slide 25
What should be written in the document:
Name of document
Name of company, department or division of the maker
Document number
Page and number of pages of document
Number of revision
Date of approved
Name and signature of the person who prepared the document
Names and signatures of the person who reviewed and person approved the document
Body of document
Document receiver
CONTENT OF DOCUMENT
Notes: <number>
<footer>
<header>
<date/time>
Format for document
Name of document _____________________ page ... of ....
Document number ________
Title _____________________________________________
Revision number ________
Written by _______________________ Edited by_______________________
Authorization signature __________ Department _______ Date ___________
Effective date _______________________ Replaces ____________________
Purpose:
Why:
Why is this procedure written.
Why is it being performed.
Scope
When:
Indicate when this procedure needs to be performed.
Where:
Indicate where this procedure applies.
Responsibility
Who:
Who performs the procedure, who is responsible to see it is performed correctly.
Materials and equipment
What: What is needed to perform the test. The list should be complete and specific.

## Slide 26
NUMBERING SYSTEM
Every document should have a number from the Control Division
Document numbering system should be made, to make easy on saving and controlling the document
Notes: <number>
<footer>
<header>
<date/time>
There are also the identification systems or codes devised to number and track both information and documents.
These are SOP numbers, equipment numbers, form numbers, receiving codes, and batch/lot numbers.
These numbering systems should be designed so that procedures, processes and materials can be traced throughout the data records.

## Slide 27
DOCUMENT CORRECTION
When correction on document is needed, please do the following actions :
  original entry not lost (draw a line across the original entry)
  close to original entry
  initialed / dated for correction
  computerized : - password
- dedicated person
Notes: <number>
<footer>
<header>
<date/time>
If the document is a process record, it should be filled in clearly and legibly. The writing should be indelible, i.e. in pen, not pencil. Any alterations must be made by putting a single line through the incorrect information, signing it and putting in the new information. There should be no use of correcting fluid or similar products. If an alteration is made, then the reason for the alteration should also be given. This is particularly important where a laboratory test result is changed – the reason for the change must be given.

## Slide 28
DOCUMENT CONTROL
Documents should be dated and authorized
  approved, signed and dated by appropriate authorized persons
  no document should be changed without authorization
All document records should be completed as the process proceeds.
Distribution list of documents should be recorded
Obsolete documents should be :
  taken from users , based on distribution list
  marked “obsolete”, archived
Create a list of running documents , centralized .
Use only updated documents
Notes: <number>
<footer>
<header>
<date/time>
Documents should be designed, prepared, reviewed and dated by appropriate authorized persons. No document should be changed without authorization.
It is essential that documents are completed as the process proceeds. Inspectors should examine documents in progress for signs of either pre-process completion or post-process completion.
Any alteration made to a document should be signed and dated; the alternation should permit the reading of the original information. Where appropriate the reason for the alternation should be recorded. For example, the error of signing the documentation for flaming lipstick products before the product packed into its tube containers.

## Slide 29
Distribution of documents should be the up-to-date documents
Copy of documents should be distributed to relevant parties
The list of distribution should be made
Document Data Control Division or QC can distribute the document
Main document should be received by Production and Quality Control Department
Supporting document is distributed to related division only
DISTRIBUTION DOCUMENT
Notes: <number>
<footer>
<header>
<date/time>
Distribution of documents needs to be carefully controlled in order to ensure that the most up-to-date version is always being used. There should be a distribution list, if appropriate, attached to the document. Unauthorized photocopying of original documents should be actively discouraged. Some companies manage this by having part of the front page printed in colour, or by using an official stamp or other means of identification.
There should be an SOP for distribution, retrieval and preparation of documentation. A document register is required. This ensures that change control over all documents is properly managed.

## Slide 30
Should be made periodically, or if needed
Obsolete documents should be retrieved from all relevant parties and its original copy should be archived
The date of revision should be stated in the new documents
Every revision should be approved by authorized person
REVISION & RENEWAL
Notes: <number>
<footer>
<header>
<date/time>
Documents should be reviewed regularly; however, the definition of “regular” will vary from company to company and with the document in question. Although not a GMP text requirement, it is useful for all master copies to have a review-by date. Alternative methods of identifying the need for review include diaries or electronic reminders. The key is to have a system.
Once the review date is reached, if no changes are required, the document should be annotated to show that it has been reviewed and the review-by date amended. If amendment of the document is required, there should be a history of the changes attached at the end. In the case of changes being made, it is important that all old copies are withdrawn and replaced by the new ones. (This confirms the previous point about the need for controlled distribution).
To correct errors :
Line-through an incorrect entry
Add the correct entry
Annonate the reason for the change or correction, and
Initial/date the correction

## Slide 31
“Do Not” Rules
DO NOT scribble out mistakes (obscures entry)
DO NOT write correct entries over incorrect entries (writing over obscures original entries)
DO NOT forget to enter all required info
DO NOT forget to initial and date entry
DO NOT use colored ink/pencil
DO NOT leave mistakes uncorrected (check your entries)
RECORD KEEPING RULES

## Slide 32
MANUFACTURING
DOCUMENTS

## Slide 33
QUALITY MANUAL
Testing
Method
Note :
Blue : WI (standard, specification & procedure)
Red : record
Product Destruction Record
Return Product Handling Record
Recall Record
Product Complaint Record
Batch Production Record
Distribution Record
Master production
document
Master Formula
Master Prod. Procedure
Master Pack. Procedure
TYPE OF GMP DOCUMENTS
Specification/ Standard
S.O.P.
Validation Protocol
Report
Work Protocol
(WP)
Raw & packaging material
Bulk
Finished product
Testing result record and report
Stability test record
Sampling record
Microbial and particle monitoring record
Equipment Status
Material Status
Product Status
Identity/
Label
Notes: <number>
<footer>
<header>
<date/time>
This slide summarizes all the types of documents that are listed in the ASEAN GMP text.
  There must be a master formulation for all manufacturing processes and a packaging instruction for each stock-keeping unit that is produced.
  Specifications and testing procedures are required for all starting materials, packaging materials, intermediates, bulk and finished products.
  Labels are required for all containers, equipment and premises.
  Batch processing documents and records are required for all manufacturing processes.
  Batch packaging documents and records are required for packaging operations.
  Standard operating procedures (SOPs) are required for all operations that are not product-specific, whether related directly to manufacturing or to operation of the facility.
The following of other documents that are useful and frequently found:
  Stock control records are usually used for all materials that are stored in the warehouse.
  Distribution records are usually used for all batches of material that are dispatched from the warehouse.
  A water quality manual describes all aspects of the water system design, operation, maintenance and water quality testing.

## Slide 34
Specifications describe the required characteristics or composition of a product or material or test, while test procedure is required to evaluate the specific characteristic performance
These kinds of documents provide the specific details defining :
  the quality of incoming materials,
  the quality of the production environment,
  the quality of the production and control process, and
  the quality of the final product.
Specification covers :
  starting materials,
  intermediate,
  bulks and
  finished products
All specifications should be approved by authorized personnel (QC manager)
SPECIFICATION
Notes: <number>
<footer>
<header>
<date/time>
Specifications and test procedures will be used by the QC department and are generally located in the laboratories.
Test procedures must be validated or verified for the available facilities before they are used for routine testing. Compendial methods need to be verified. This means that the method is demonstrated to give correct results in the laboratory facilities available. Specifications will include tests for identity, content purity and quality. Specifications should be dated and authorized. The responsibility for their issue and maintenance rests with the QC department. It may be necessary to update the documents occasionally in line with national compendiums or the company's requirements. Written specifications are required for all starting and packaging materials including water in all its various standards.

## Slide 35
All raw and packaging materials specification should consist of the following data:
Name of material
Name of principle manufacturer or supplier
Description of the material
Testing parameters and acceptance limit
Shelf life and retest date
Technical drawing, if applicable
Special precaution (storage condition & safety condition)
STARTING MATERIAL SPECIFICATION
Notes: <number>
<footer>
<header>
<date/time>
The minimum requirements for starting materials are:
  INCI name and internal code reference
  Reference to pharmacopoeia monograph if appropriate
  Test parameters and acceptance criteria
  Other information may include details of supply, testing methodology and storage conditions.
For packaging materials, there should be reference to compatibility with the product. For all materials, the frequency of retest should be specified. If intermediates or bulk products are either purchased or dispatched, then they will need a specification. One will also be required if the data obtained from these materials are going to be used in the assessment of the finished product. They will be similar to the specification for the starting material or finished product, as appropriate.

## Slide 36
All specifications of intermediate, bulk and finished products should describe the following :
  Name of product
  Description (example cream, gel, liquid, etc)
  Physical properties (e.g. color, odor, viscosity, density)
  Chemical & microbiological assays and their acceptance limit, if necessary
  Retest date
  Storage condition and safety precaution, if necessary
PRODUCT SPECIFICATION
Notes: <number>
<footer>
<header>
<date/time>
Specification for finished products, the specification should include the following information:
  Product name and internal code reference
  Name of the active ingredients, if any
  The formula (or a reference to it)
  Sampling and testing methodology
  Test parameters and acceptance criteria
  Storage conditions
  Shelf-life or stability data

## Slide 37
MASTER FORMULA
The master formula should be available upon request.
A printed master formula and manufacturing instructions for each product must be prepared, endorsed, and dated by the owner, manager, or competent person delegated by management. Wherever possible a second competent person should check, reconcile, endorse, and date formula instructions.
The master formula can be divided by :
  processing master formula
  packaging master formula
Transcription from the master documents should be by photocopying or computer printout. A competent person should initial each document before issue to signify that it is complete, legible and appropriate. Instructions should preferably be printed.
Notes: <number>
<footer>
<header>
<date/time>
Special requirements:
There must be a formally approved master formula for each product that is manufactured, in each batch size.
Both manufacturing master documents are used as references in the development of processing records.
They should be located in quality control and production departments.
The master formula is frequently used as the master batch-processing document. It is often photocopied to provide the individual batch-processing document. Whatever method is used, it must ensure that there can be no transcription error.
The batch-processing document is never a hand-written copy.
The same method can be used to prepare the batch packaging document.

## Slide 38
The master processing documents should include at least the following :
  product name
  batch size
  a description of the product (form, color, odor, etc)
  a list of all materials and the quantity to be used
  equipment to be used and processing location;
  theoretical or expected yield;
  adequate step-by-step directions for manufacture:
    precautions to be taken with regard to product and personal safety
    equipment to be used and how to clean it to prevent cross-contamination;
    sequence of adding materials;
    mixing times, temperatures;
    in-process control and storage condition
PROCESSING MASTER FORMULA
Notes: <number>
<footer>
<header>
<date/time>
The information of processing master formula that it should contain includes the following:
  Name of the product with product reference code
  Dosage form and batch size
  A full list of materials including quantities and unique reference code for each
  Expected final yield with acceptable limits (plus intermediate yields)
  Processing location and principle equipment
  Methodology for equipment preparation (cleaning, calibration, etc......)
  Stepwise and detail steps of processing instructions (space for operator to sign, check signature, recording of times, quantities, temperatures, etc......)
  Details of in-process controls with instructions for sampling and acceptance limits
  Storage requirements and any special precautions.

## Slide 39
PACKAGING MASTER FORMULA
The master packaging documents must include at least the following where applicable:
  the name of the product;
  the contents of the primary container by volume or weight;
  a reference to the specification of all materials required for the packaging and labelling of the product;
  any special instructions or precautions, including area clearance check
  Description of packaging process;
  In-process control, with sampling instruction;
  provision for calculation of yield or reconciliation.
An accurate copy of the master packaging and labelling instructions must be made for each batch of product before it is manufactured.
Notes: <number>
<footer>
<header>
<date/time>
The packaging instruction is the similar to the master formula, but covers packaging rather than manufacturing. There should be one document for each product and pack size. The information that it should contain includes:
  Name of the product
  Dosage form and method of administration
  Pack size (number, weight or volume of product in finished pack)
  List of all packaging materials (quantities, size and code number).
  Examples of printed packaging materials, with location of batching information
  Special precautions, including area clearance checks
  Description of the packaging operation
  In-process control checks, with sampling instructions and acceptance criteria.

## Slide 40
LABELING SYSTEM
Labeling systems are used to identify :
  the status of the material, product, equipment , laboratory reagent, or facility
  restricted areas, and
  warning labels.
There are 2 classes of labels :
  label for finished products
  label used within the factory to control process
Reference standards (both primary and secondary) must be appropriately labeled and the issuance must be controlled
Notes: <number>
<footer>
<header>
<date/time>
Labels include :
raw material tags,
quarantine labels, release labels, reject labels,
labels to identify specific storage areas,
biohazard or danger material labels,
restricted access labels,
equipment "cleaned" or "waiting for cleaning" labels,
process intermediate labels, and
the final product labels.
These permit the identification and tracking of materials, of the progress of a production process, and assurance of the proper functioning of equipment.
Labels are required for all containers of materials, whether for starting materials, intermediates or finished products; there must be sample labels and labels that are applied to materials that have been sampled; there must also be labels for all process equipment and for premises that are in use for manufacturing. The labels should be clear and unambiguous. Where possible, it is advisable for companies to use colours to indicate status (quarantine, accepted, rejected, cleaned or dirty).
Companies generally have their own systems for internal labelling that define what information is carried, but for finished products, there is a national requirement. Responsibility for labelling varies with company practice, but the process is generally overseen and controlled by the QC department. QC staff are responsible for issuing status labelling when a material has been approved or rejected. The responsible production and/or QC staff should sign labels stating that equipment is clean and available for use.
There are two classes of labels :
There are the finished product labels, which must meet ASEAN cosmetic regulatory authority requirements as specified in the marketing authorization.
Then there are the labels used within the factory to control processes.

## Slide 41
Another type of documentation is the form used for recording data as it is taken during the performance of tasks, tests, or events.
These are forms (datasheets, or data record forms), reports, batch processing records, and equipment log books.
These documents provide the evidence that the raw materials, facility environment, the production process, and the final product consistently meet the established quality requirements.
Record legibly in permanent ink
GMP RECORDS
Notes: <number>
<footer>
<header>
<date/time>
Another type of documentation is the form used for recording data as it is taken during the performance of tasks, tests, or events. These are forms (datasheets, or data record forms), reports, batch processing records, and equipment log books. These documents provide the evidence that the raw materials, facility environment, the production process, and the final product consistently meet the established quality requirements.

## Slide 42
Check whether control records are maintained for:
  Raw materials and primary packaging materials, documenting disposition of :
    released materials
    rejected materials.
  Manufacturing of batches, documenting the:
    kinds, lots and quantities of material used.
    processing, handling, transferring, holding and filling.
    sampling, controlling, adjusting and reworking.
    code marks of batches and finished products.
  Finished products, documenting sampling, individual laboratory controls, test results and control status.
  Distribution, documenting initial interstate shipment, code marks and consignees.
RECORDS MAINTENANCE

## Slide 43
Should be prepared for each batch of product.
Each Batch Processing Record should include the following :
  name of product
  batch or code number
  batch formula
  brief processing process
  processing date and yield
  identity of individual major equipment & lines or location used
  records of cleaning of equipment used for processing as appropriate
  in-process control and laboratory results, such as pH and temperature test records
  any sampling performed during various steps of processing
  any investigation of specific failure or discrepancies
  results of examinations on bulk products
BATCH PROCESSING RECORD
Notes: <number>
<footer>
<header>
<date/time>
A batch processing record is required for each batch of material produced. The review of this document is a critical part of the batch release process. A master document should be prepared for each batch size that will be manufactured. It will be taken from the relevant parts of the master formula as discussed previously.
The first step in this document must be the area clearance check. This is a record of the previous product and batch processed in the area and a confirmation that all the material and documentation relating to that batch has been removed. It is also confirmation that all the cleaning has been carried out correctly. This check must always be documented.
The batch processing record is both a detailed instruction to the operator of the activities that must be carried out during manufacturing and a record that these activities have been carried out. It should be filled in at the time that processing takes place. Critical activities require a check signature from a second person (either from production or QC as appropriate) to confirm that the information recorded is accurate.
The information required in the batch processing record includes:
  Name of the product
  Batch number
  Dates and times for major steps in the process
  Name of person responsible for each stage of production
  Name of operators carrying out each processing step and check signatures if required
  Theoretical quantities for materials in the batch
  Reference number and quantity of materials used in the batch
  Main processing steps and key equipment
  In-process controls carried out, and the results obtained
  Yield at each stage with comments on deviations
  Expected final yield with acceptable limits
  Comments on any deviations from the process.
Information that does not change, such as the product name, process steps and theoretical quantities of material, can be printed on the master copy. Variables, such as actual quantities of materials used and yields are entered by the operators during the manufacturing process.

## Slide 44
BATCH PROCESSING RECORD
The manufacture of the batch must proceed in accordance with these documents, and the following must be included:
  the actual weights of materials and, where given, the unique identifying number. These weights should, where possible, be independently checked, and both weigher and checker should initial the record sheet;
  the initials of the operator or supervisor for each step immediately after it has been performed;
  the actual yield;
  a record of all samples taken and the results of tests performed;
  the batch number which specifically identifies it and distinguishes it from all other batches;
  where applicable, a date after which the product must not be used.

## Slide 45
Should be prepared for each batch of product.
Each Batch Processing Record should include the following :
  name of product
  batch & code number
  batch formula and brief packaging process
  packaging date
  Theoretical and actual yield
  identity of individual major equipment & lines or location used
  records of cleaning of equipment used for packaging process
  in-process control and laboratory results, such as volume and product weigh
  packaging line clearance records
  Expiry date, if shelf life is less than 30 months
  any investigation of specific failure or discrepancies
  disposition and identity of quarantine label
BATCH PACKAGING RECORD
Notes: <number>
<footer>
<header>
<date/time>
The batch packaging record is required for every batch or part batch that is packaged. It is developed from the relevant part of the packaging instructions and, once again, its review is an important part of the batch release process. Depending on company practice and the design of the document, it may be specific to a particular batch size or may be used for a variety of sizes.
The information required for the completed batch packaging record, once again, consists of a combination of pre-printed material and data that are added by the operators during the process:
  Name of the product, batch number and quantity to be packed
  Batch number, theoretical quantity and actual quantity of finished product
  Reconciliation calculations
  Dates and times of operation
  Name of person responsible for packaging
  Initials of operators carrying out each step
  Checks made and results obtained
  Details of packaging operation, including equipment and line used
  Returns to store
  Specimen of printed packaging materials, with batch coding
  Comments on deviations from the process and actions taken
  Reconciliation of packaging materials, including returns and destruction.
If returns to the stores are permitted for printed packaging materials, they should first be checked to make sure that they have not been batch coded. A QC signature is required as part of this process, either on leaving the packing hall or on being received in the stores. If excess materials are destroyed, there must be a record of the quantities on the batch documentation. There should also be a procedure covering destruction, including methods and responsibilities. Reconciliation is of vital importance since it helps to confirm that the batch has been processed correctly. Any significant variation in materials should be taken as an indication that there could be a problem. Inspectors should check for investigation of these variations before the batch is signed off.
Finally, area clearance checks should show no foreign materials are carried over from one operation to the next.

## Slide 46
Record for each testing, assay result and release or rejection of starting materials, intermediates, bulk and finished product should be maintained.
QC record may consist of :
  date of test
  identification of the material
  supplier name
  date of receipt
  original batch number if any
  batch number
  quality control number
  quantity received
  date of sampling
  quality control results
QUALITY CONTROL RECORD

## Slide 47
RELATED HYPERLINK DOCUMENTS
Trainer Manual of Documentation
Guidance to Create SOP
Guidance of Numbering System
Guidance of Change Control
Starting Material Reception and Stock Card
Material / Product / Equipment Status Labels
Electronic documentation

## Slide 48
REFERENCES
ASEAN Guidelines for Cosmetic GMP (2003)
WHO EDM, Basic Principle of GMP: Documentation part 1 and 2 (2004)
Wirjadidjaja E.C, Good Documentation Practices, Jakarta (March 2005)
Soenardi F, Document Creation, Jakarta (March 2005)

## Slide 49
Thank You