## Slide 1: ASEAN GMP SUPLEMENTARY TRAINING MODULE CONTAMINATION & GOOD HOUSEKEEPING
Prepared by :
Nuning S. Barwa - Indonesia
Ofelia M. Malagkit - Philippines
Haryanto Susilo - Indonesia

## Slide 2
A key principle in understanding contamination control is to realize that it is much easier to fix a contamination problem prior to it entering your system rather than trying to fix it after a system has been contaminated.
Contamination can be prevented by practice good sanitation and hygiene .
An ounce of prevention is better
than a pound of cure.
<number>
KEY PRINCIPLES

## Slide 3
KEY ISSUES OF
CONTAMINATION

## Slide 4
Particulate contamination
Cross contamination, mix-ups and errors
Foreign matter contamination
Microbial contamination
<number>
TYPE OF CONTAMINATIONS

## Slide 5
There are two primary types of particulate contamination :
  Organic particulates.
  These consist primarily of human body parts such as hair, dandruff flakes, skin cells, sweat, etc.
  Particles generated during one of manufacturing process, water handling, probing, storage, such as dirt, dust, lint, fibers
<number>
Type of Contamination
PARTICULATES CONTAMINATION

## Slide 6
Cross-contamination caused by:
  ventilation system not properly filtered
  container not sealed tightly
  mix-up of left-over components
Airborne powder from component A
We can avoid this CGMP violation by carefully following our SOP’s when cleaning premises, equipment and containers.
<number>
left over
component A
Type of Contamination
CROSS CONTAMINATION

## Slide 7
Contamination comes from :
Food & drink
Residue
Cleaning materials
Lubricants
Machine parts
Pests
<number>
Type of Contamination
FOREIGN MATTER CONTAMINATION

## Slide 8
Microorganisms means yeasts, molds, bacteria, and viruses and includes, but is not limited to, species having public health significance.
The term “undesirable microorganisms” includes those microorganisms that are of public health significance, that subject cosmetic to decomposition, that indicate that product is contaminated with filth, or that otherwise may cause product to be adulterated within the meaning of the act.
Occasionally in these regulations, FDA used the adjective “microbial” instead of using an adjectival phrase containing the word “microorganism”.
<number>
Type of Contamination
MICROBIAL CONTAMINATION

## Slide 9
Prevent the generation and dissemination of dust during production of dry product .
Contamination of a starting material or of a product by another material or product has to be avoided.
This risk of accidental cross-contamination arises from the uncontrolled release of dust, gases, vapors, sprays, or organisms from materials and products in process, from residues on equipment, from intruding insects, operators' clothing, skin, etc.
Among the most hazardous contaminants are highly sensitizing materials, biological preparations such as living organisms.
e. Production areas where susceptible products are processed should undergo periodic microbiological monitoring.
CONTAMINATION PREVENTION (1)
Notes: Prevention of contamination should be done in every step of manufacturing processes , it can be happened in the step preparation, weighing , mixing, filling etc. especially for dry product , dissemination of dust during production should be minimized . Type of contaminant can vary , starting form dust ,gases, vapors , spray, residues on equipment, insect , tissue, operators clothing. Area where some susceptible products are processed , such as product for babies or products applied surrounding eye area should be monitored periodically for its microbial population.

## Slide 10
f. Cross-contamination should be avoided by appropriate technical or organizational measures, for example:
  production in segregated areas, or by campaign followed by appropriate cleaning;
  providing appropriate airlocks, or pressure differentials;
  wearing protective clothing in areas where products with special risk of cross-contamination are processed;
  using cleaning and decontamination procedures of known effectiveness, as ineffective cleaning of equipment is a common source of cross-contamination;
  using a "closed system" of production;
  using cleanliness status labels on equipment
Measures to prevent cross-contamination and their effectiveness should be checked periodically .
CONTAMINATION PREVENTION (2)
Notes: Prevention of cross contamination can be done either using technical or organizational measures . It can be in the form of campaign process , segregation area and machines , used of closed system. In fact , choice of method used for this prevention will depend on the size of enterprise , availability of equipment , source of budget etc.
Monitoring the prevention for cross contamination and its effectiveness should be made periodically.

## Slide 11
GOOD HOUSEKEEPING
PRACTICES

## Slide 12
Cleaning operations shall be performed in a manner to prevent contamination of materials and products.
Only cleaning compounds and sanitizers authorized for food contact surfaces shall be used for cleaning. Appropriate verification procedures or testing shall be done periodically to insure that the concentration of Clean-In-Place (CIP) and other cleaning chemicals are consistent with the product labelling.
When not in use, all cleaning compounds and sanitizers shall be properly labelled and stored in a locked compartment, away from production and storage areas.
Cleaning equipment and tools shall be supplied and be readily available for use. All cleaning equipments shall be maintained and stored in such a way as not to contaminate product or equipment.
<number>
Avoid Contamination
CLEANING PRACTICES

## Slide 13
Description of cleaning can be divided by :
“Deep cleaning” shall be assigned to the appropriate department(s) for germ removal, and shall be accomplished by and consistent with a Master Cleaning Schedule.
Daily “Housekeeping or Cosmetic Cleaning” shall be assigned to the appropriate departments and shall be undertaken to ensure work and support areas are maintained during normal working hours. All such operations should be undertaken in a manner to prevent contamination.
“Maintenance cleaning” shall be assigned for maintenance purpose
BASIC DESCRIPTIONS

## Slide 14
Every personnel responsible to keep the cleanliness of working place
Class 3
Class 2
Class 1
CLEANLINESS PRINCIPLES

## Slide 15
“Good housekeeping”
shall be maintained at all times.
Area and products shall be free from dust, dirt, cobweb garbage materials
Formal housekeeping inspections shall be done
Cleaning materials shall be kept in designated areas
<number>
CLEANLINESS PRACTICES (1)

## Slide 16
Buildings, fixtures, and other physical facilities of the plant shall be maintained in a sanitary condition and shall be kept in repair sufficient to prevent product from becoming adulterated within the meaning of the act.
Cleaning and sanitizing of utensils and equipment shall be conducted in a manner that protects against contamination of cosmetic product, product-contact surfaces, or product-packaging materials.
CLEANLINESS PRACTICES (2)

## Slide 17
Processing area
Packaging area
Locker
Laboratory area
GOOD HOUSEKEEPING

## Slide 18
Keep work area clean & orderly
Protects the quality of materials and products;
Minimizes errors and prevents contamination;
Ensures safety in the workplace.
BENEFIT GOOD HOUSEKEEPING

## Slide 19
A Clean Workplace is High in QUALITY;
A Clean Workplace is High in PRODUCTIVITY;
A Clean Workplace Keeps COSTS Down;
A Clean Workplace Saves TIME;
A Clean Workplace Ensures EFFICIENT Delivery;
A Clean Workplace Provides HEALTHY environment;
A Clean Workplace is SAFE for people to work in;
A Clean Workplace is High in MORALE.
Before cleaning program
After cleaning program
ADVANTAGES GOOD HOUSEKEEPING

## Slide 20
REFERENCES
ASEAN Guidelines for Cosmetic GMP (2003)
Barwa, N.S. Good Housekeeping, Jakarta (2000)

## Slide 21
Thank You