## Slide 1: SUPPLEMENTARY ASEAN GMP TRAINING MODULE PEST CONTROL
Prepared by
Ofelia M. Malagkit ~ Philippines
Approved by
ASEAN GMP Team
Endorsed by
ASEAN Cosmetic Committee

## Slide 2
Environmental Hygiene
“Pest Control Program”
Meeting of pest attack strategy
<number>

## Slide 3
Environmental hygiene and its implementation will depend on the area where the manufacturing plant is situated.
The precautions to be taken will be different if the site is in a town or in the country.
The main principles of environmental hygiene will consist of:
proper fencing (public, dogs, etc.)
pest control (rodents, insects, birds)
liquid and solid waste disposal
<number>
PRINCIPLE OF ENVIRONMENTAL HYGIENE

## Slide 4
Pest Control Program should be in place, that includes regular treatment against termites, ants, cockroaches, and rodents.
Pests (insect, rodents and birds) should be controlled to prevent their access to cosmetic plant , production areas and storage departments.
This is best achieved by the construction of buildings and working places where access of insects, rodents and birds is hindered, but it will be almost impossible to secure buildings totally against pests.
However good design and construction may delay the entry of pests which is a worthwhile objective of an overall rodent control programme. Even if the buildings are well-constructed and as pest-proof as possible it will be necessary to have a regular pest control.
<number>
PEST CONTROL PROGRAM

## Slide 5
Good housekeeping and proper sanitation are the key to any type of long range pest control.
A formalized preventive pest control program shall be maintained in the plant and well documented.
The pest control program may be undertaken by trained in-house personnel or be provided by an outside certified pest control contractor.
Pest monitoring devices and appropriate integrated pest management strategies should be properly used to provide ongoing monitoring for pest activity and to design an effective control program to eliminate pests and the potential for pest activity.
<number>
KEY ISSUE PCP (1)

## Slide 6
The plant shall maintain written procedures outlining the requirements of the program to reduce the potential for product contamination from pest activity or the use of materials and/or procedures designed to control pest activity.
Pest control activities shall at all times be conducted in total compliance with the regulatory requirements of the agency controlling such procedures.
The programs should include a minimum pesticide applications
<number>
KEY ISSUE PCP (2)

## Slide 7
If the pest control program will be done by in-house trained personnel, he/she shall :
  a. maintain a file of sample labels and chemical safety data information for each pesticide used and shall maintain pesticide usage records as well as records on maintenance of the safety and protective equipment used.
  b. maintain and enforce written procedures for the application of all pesticides.
  c. maintain accurate records of application of pesticides
<number>
IN-HOUSE PCP

## Slide 8
If the program is done by a contracted licensed pest control company, we shall maintain the following:
A contract describing the specific services to be rendered, including materials to be used, methods, precautions, and chemical safety data information required by government regulations.
Sample labels for all pesticides used.
Accurate and complete service records describing current levels of pest activity and recommendations for additional efforts needed to correct conditions allowing a potential for pest activity.
Accurate documentation of all pesticide applications, including rodenticides, made in or around the plant.
<number>
CONTRACTED PCP

## Slide 9
Documentation shall be maintained in accordance with government regulations and must document, at a minimum:
  Materials applied
  Target organism
  Amount applied
  Specific area where pesticide was applied
  Method of application
  Rate of application or dosage
  Date and time treated
  Applicator’s signature
<number>
PEST CONTROL PROGRAM

## Slide 10
All manufacturers shall establish effective preventive programs for the elimination of pest activity. The effectiveness of the programs will be measured by the lack of observation of pest activity and evidence.
Rodent burrows, rodent runs, and any conditions attracting rodents or other pests both inside and outside the plant shall be eliminated.
Specific procedures include but are not limited to:
  Outside bait stations for the control of rats and mice.
  Internal control program which shall comply with government regulations
  Rodent burrows, rodent runs, and any conditions attracting rodents or other pests both inside and outside the plant shall be eliminated.
  Electric flying insect monitors should be used as needed to identify flying insect entry into the plant.
  Birds shall be controlled by exclusion
PEST CONTROL PREVENTIVE PROGRAM

## Slide 11
All pesticide containers and application equipment shall be properly labeled to identify the contents. Insecticides or herbicides each require separate equipment for application. All equipment used for pesticide application shall be properly maintained in serviceable condition.
Pesticides stored in a plant shall be stored in a locked enclosure, preferably in an outside building away from production areas.
Easily understandable labelling warning of the contents and limiting access shall be posted on the exterior entrances to this enclosure.
The storage enclosure shall be adequate in size and construction and well ventilated. The enclosure shall contain the necessary materials to control spills or leakage and to avoid injury to personnel.
Disposal of pesticides, pesticide containers and pesticide residues shall be done in a manner that meets all regulatory guidelines and must be consistent with the instructions included on the label for the material.
<number>
SAFETY PEST CONTROL PROGRAM

## Slide 12
Principles in insect control program may be:
  Biological control through emphasis on the natural enemies of pests.
  Cultural control through alteration of the environment to make it unfavourable to pests. Sanitation programmes and water management are examples.
  Physical and mechanical control, for example burning and using sticky adhesives.
  Autocidal control, disrupting the breeding cycle of a pest (release of sterilized male insects or genetically altered insects).
  Behavioural control, which involves the identification, production, and application of chemical attractants which draw the insects to a trap or interrupt and confuse breeding patterns.
  Chemical control, which is the most obvious control method, but also the most controversial of all control methods. This method includes chemical insecticides but non-chemical methods should be employed if possible.
These principles can also be used for the control of rodents and birds but the slower generation time of these animals reduces some of the above-mentioned alternatives.
<number>
INSECT CONTROL PRINCIPLE

## Slide 13
The most effective way to control rats is to separate them from food supplies forcing the rats to migrate in search of food thus depressing the reproduction rate.
This can only be done through careful management of hygiene standards in plant cosmetic production.
Other principles in rodent control are:
chemical control
physical control
biological control
<number>
RODENT CONTROL PRINCIPLE

## Slide 14
The most used method for chemical control of rodents is to prebait which overcomes most problems of shyness and avoidance when baiting. In prebaiting a non-poisoned bait is introduced for a rat population over a period and then the non-poisoned bait is replaced with the identical poisonous variety of bait.
The rodenticides used as baits can be divided into two main types:
  multiple dose of chronic chemicals, and
  single-dose (acute) rodenticides.
  According to the situation, each type can be recommended.
The type of bait station used will depend on its location. It is important to prevent spread of rodenticides in the production areas and the bait stations must be inspected regularly.
Chemical control may include the use of rodenticides as tracking powder. These materials kill rats when the animal grooms itself after having been in touch with the powder. Tracking powders (like other baits) should not be used in production areas.
<number>
Rodent Control Program
CHEMICAL CONTROL

## Slide 15
Physical control
The best known method of physical control is traps. Trapping is of special importance in an environment where cosmetic product is produced, handled or stored because poisonous baits cannot be used for safety reasons.
Biological control
Rodents (rats) have natural enemies such as cats and dogs, but these animals should not be permitted to control (kill) rodents in cosmetic production areas.
<number>
Rodent Control Program
PHYSICAL & BIOLOGICAL CONTROL

## Slide 16
Outside bait station for the control of rats and mice :
Baits used shall be approved registered rodenticide or monitoring (non-toxic) feeding blocks.
These bait stations should meet tamper resistance standards and shall be properly positioned, anchored in place, locked, and properly labeled in compliance with regulatory requirements. The bait stations shall be installed around the exterior perimeter of the plant at 50-100 foot (15-30 meter) intervals.
Where allowed by local ordinance, the stations should also be installed along the fence line in accordance with industry best practice.
All stations shall be inspected and serviced no less than once per month. Each service and the results of the service will be documented for each station or device and maintained on file.
<number>
Rodent Control Program
OUTSIDE BAIT STATION

## Slide 17
Internal measures shall comply with government regulations. Unless prohibited by regulatory requirements, internal control programs shall consist of the use of mechanical traps, extended trigger traps, or glue boards, but should not include feeding stations of any kind.
In countries where mechanical traps and/or glueboards are prohibited by law, internal feeding stations containing non-toxic bait may be used for monitoring purposes. These feeding stations shall be used in a manner consistent with the label directions for the bait and in a manner that minimizes the potential for contamination of the cosmetic products or materials in storage.
These stations shall contain only non-toxic bait, unless evidence of rodents has been documented in the recent past. If activity has been found, toxic bait can be used until the activity is eliminated. Non toxic bait should then be reinstalled in the stations for routine monitoring purposes.
These stations should be constructed of a durable material such as hard plastic and should be kept locked and secured to keep them in place.
<number>
Rodent Control Program
INSIDE BAIT STATION

## Slide 18
It is recommended that the internal devices used for routine monitoring purposes be positioned at 20-40 foot (6.5-13 meter) intervals along exterior perimeter walls.
Where possible, rodent control devices should be installed at each side of exterior overhead and pedestrian doors or where there is a potential for rodent entry into the plant.
In any area where there is a potential for rodent activity, such as raw material storage areas within a plant, rodent control devices should be installed along interior walls.
The contractor or plant personnel shall inspect and clean the devices at least once a week.
<number>
Rodent Control Program
LOCATION OF BAIT STATION

## Slide 19
Maps or schematics showing the locations of the rodent control devices shall be maintained and kept current.
A record of the service and cleaning of each rodent control device shall be maintained in each device. The service documentation should include the findings from the device inspections.
<number>
Rodent Control Program
MAPS STATION

## Slide 20
Pesky birds make bad neighbours because they are a potential health risk. Bird droppings and bird nests carry various diseases that can be passed on to people and pets. Their nests are home to numerous parasites such as mites, fleas, ticks and pathogens.
The best control is to prevent the birds from having access to buildings. It is important to understand the relationship between birds and their environment.
Bird attractants may be food supplies, water, special vegetation around buildings, etc. and these attractants must be removed or modified.
Toxicants, shooting and trapping may be used to control birds.
<number>
BIRD CONTROL PRINCIPLE

## Slide 21
Flying pest control program can be described as follow:
Birds shall be controlled by exclusion: netting, screening, mechanical traps, if legal and practical.
Electric flying insect monitors should be used as needed to identify flying insect entry into the plant. Units should be installed so that insects are not attracted from outside the building. Units should not be placed within 10 feet (3 meters) of exposed product on a production or packaging line.
All units should be listed on the Master Cleaning Schedule for cleanout on a weekly schedule during peak insect season. They can be cleaned monthly during off-peak season.
Electronic insect control
Electronic insect killer
<number>
FLYING PEST CONTROL

## Slide 22
Insect and rodent control program shall include:
Facility layout showing pest control and bait stations
Checklist reflecting the steps and areas to be treated
Frequency of inspection / treatment
Responsibilities, in-house/outside agency treatment
Documentation (i.e. certificate of treatment if done by outside agency
Report on treatment done and observations noted including signatures/ approvals
Cleaning procedures before and after treatment
List of chemicals used and their concentrations (i.e. 75 ml crackdown for 5 liters water for cockroach & ant control)
Material Safety Data Sheets (MSDS) available for chemicals used.
<number>
INSECT & RODENT CONTROL

## Slide 23
<number>
CONCLUSION

## Slide 24
<number>
ASEAN Guideline for Cosmetic GMP, 2003
WHO Basic Principle of GMP : Sanitation & Hygiene, 2000
Bishop, Basic Principle of Sanitation, N.E.M. Business Solutions, 1997
Health Services Agency, County of Santa Cruz, Cross Contamination, 1999
www.fao.org
www.maintenanceconference.com
REFERENCES

## Slide 25
Thank You