## Slide 1: ASEAN GMP TRAINING MODULE SANITATION & HYGIENE
Prepared by
Ofelia M. Malagkit - Philippines
Approved by :
ASEAN Cosmetic GMP Team
Endorsed by:
ASEAN Cosmetic Committee

## Slide 2
CONTENT OF PRESENTATION
Basic description
  Introduction
  Objectives
  Scope
  Basic cleaning principles & practices
Personnel hygiene
Sanitation of premises
Sanitation of equipment
Conclusion
References

## Slide 3
BASIC DESCRIPTION

## Slide 4
High level of hygiene and sanitation shall be practiced in every aspect of manufacturing cosmetic products.
The scope of hygiene and sanitation covers personnel, premises, equipment, apparatus, production materials and containers, and environment.
Any source of contamination shall be eliminated through an integrated comprehensive program of sanitation and hygiene.
In all instances, the hygiene and sanitation procedures shall be periodically assessed to ensure that the effectiveness of the operation meets the requirements.
INTRODUCTION

## Slide 5
The aim of sanitation and hygiene measures is to eliminate all potential sources of contamination and cross-contamination from all areas where the product quality is at risk.
OBJECTIVES

## Slide 6
Sanitation and hygiene should be practiced to avoid contamination of personnel and during manufacturing of products.
It should cover all aspects of manufacturing:
  Personnel
  Premises
  Equipment and apparatus
  Production materials and containers
  Products for cleaning and sanitation
  All potential sources of contamination
SCOPE
Notes: <number>
<footer>
<header>
<date/time>
Detail description and principle of contamination can be found in the attached hyperlink documents:
Type of contaminants :
Particulate contamination
Cross contamination, mix-ups and errors
Foreign matter contamination
Microbial contamination

## Slide 7
Cleaning and sanitation is a key consideration when designing premises and equipments to operate in a cosmetic industry.
Proper cleaning plays an important role. The methods used to establish a clean manufacturing environment vary from company to company. The goal is always the same, to acquire the level of cleanliness to maintain a high product quality while minimizing costs.
To understand the concept of cleanliness, it is necessary to define some common words used in the industry. Most important are the words clean, sanitation, hygiene, and sterile.
CLEANING PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
Definition of several concept of cleanliness :
Clean means free from dirt, stain, or impurities and general unsoiled. This is the easiest level of cleaning to accomplish and can be achieved with water and solvent flush. And condition of clean can often be measured by visual inspection.
Sanitary means free of germ. Sanitation is making something sanitary such as by sterilization. Sanitation also means the state of being clean and conducive to health.
Hygiene is the practice of keeping one’s self and one’s surrounding clean, especially for illness prevention and health maintenance.
Sterilization is the most difficult level of cleaning to be obtain. Sterilization means making some object free of live bacteria or other microorganism (usually by heat and chemical, or the act of making an organism barren or infertile. It is difficult to establish and maintain since the methods for killing these living organisms is even harsher than the methods used for obtaining sanitary condition.
Disinfection is treatment to destroy harmful microorganisms but not usually bacterial spores. This does not necessarily involve killing all microorganisms, but reducing their number to a level not normally harmful to health.

## Slide 8
Cleaning operations shall be performed in a manner to prevent contamination of materials and products.
Cleaning practices can be divided by :
  “deep cleaning”,
  “housekeeping cleaning”, and
  “maintenance cleaning”.
All cleaning compounds and sanitizers shall be properly labelled and stored in a locked compartment, away from production and storage areas.
Cleaning equipment and tools shall be supplied and be readily available for use. All cleaning equipments shall be maintained and stored in such a way as not to contaminate product or equipment.
CLEANING PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
Description of cleaning can be divided by :
  “Deep cleaning” shall be assigned to the appropriate department(s) for germ removal, and shall be accomplished by and consistent with a Master Cleaning Schedule.
  Daily “Housekeeping or Cosmetic Cleaning” shall be assigned to the appropriate departments and shall be undertaken to ensure work and support areas are maintained during normal working hours. All such operations should be undertaken in a manner to prevent contamination.
  “Maintenance cleaning” shall be assigned for maintenance purpose
Only cleaning compounds and sanitizers authorized for food contact surfaces shall be used for cleaning. Appropriate verification procedures or testing shall be done periodically to insure that the concentration of Clean-In-Place (CIP) and other cleaning chemicals are consistent with the product labelling.

## Slide 9
For personnel :
To prevent contamination risk that effect personnel health
For product :
To prevent contamination of the products
To maintain the high standard of product quality
For company :
To save on cost, avoid reworks and rejects
To avoid consumer complaints
To avoid potential product recall
For consumers :
To get safe and good quality product
BENEFITS

## Slide 10
SANITATION
HYGIENE
PERSONNEL HYGIENE

## Slide 11
Personal hygiene will usually be the main element in the term “hygiene”; the reason being obvious.
Bacteria causing diseases or spoilage may be carried and transmitted to surfaces and product by workers handling the cosmetic products.
BASIC HYGIENE

## Slide 12
All personnel working in direct contact with products shall conform to hygienic practices while on duty to the extent necessary to protect the product against contamination. The methods for maintaining cleanliness include, but are not limited to:
  Wearing outer garments suitable to the operation in a manner that protects against the contamination.
  Maintaining adequate personal cleanliness.
  Washing hands thoroughly (and sanitizing if necessary to protect against contamination with undesirable microorganisms)
  Maintaining gloves, if they are used in product handling, in an intact, clean, and sanitary condition.
  Wearing, where appropriate, in an effective manner, hair cap, beard covers, or other effective hair restraints.
GENERAL REQUIREMENTS

## Slide 13
Employees shall be encouraged to practice good personal hygiene habits at all times.
Personnel should be healthy and capable to perform their assigned duties.
Regular medical examination must be conducted for all production personnel involved in manufacturing processes.
  during recruitment process
  every regular period

X
HEALTHY & GOOD HABIT

## Slide 14
Personnel must practice good personal hygiene.
  regular bathing every day
  brushing of teeth
  washing hands
    before entering the
    production area
    after visiting the toilet
    after eating
    after smoking
GOOD PERSONNEL HYGIENE

## Slide 15
Wet your hand with flowing water
Use soap around your hand and fingers.
If needed use brush to clean your nails
Rinse your hand with flowing water
Dry your hand with tissue or hand dryer at 320 – 600C.
Don’t touch anything. If can not be avoided, repeat step 1-5
HAND WASHING GUIDELINES

## Slide 16
All authorized personnel entering the production areas should practice good personal hygiene including wearing of proper attire, suitable headwear and footwear.
To avoid cross contamination, personnel should not move between areas producing different products.
PROPER ATTIRE

## Slide 17
Personnel should wear clean attire appropriate to the duties they perform.
Design of the attire should not have:
  fiber materials
  pocket at upper part of the waist.
Personal items such as pens, pencils, or thermometers shall be carried in pockets or pouches below the waist when employees are in production areas.
DESIGN OF ATTIRE

## Slide 18
Wrong
Right
Male
Female
PROPER WEARING OF HEAD CAP

## Slide 19
Avoid direct physical contact with the product to protect from contamination.
Personnel should wear protective attire when working with hazardous materials
Dust mask
smoke mask
goggles
gloves
moustache &
beard cover
SAFETY ATTIRE

## Slide 20
Personnel who have an illness or open lesions that are likely to present a risk to the product, should not be allowed to carry out operations that involve handling of starting materials, intermediates or finished products until the condition has cleared up.
VISIBLE ILLNESS & OPEN LESIONS

## Slide 21
Personnel should be instructed and encouraged to report to their immediate supervisor when they are ill or when they see any conditions that may adversely affect the product quality.
PERSONNEL WITH ILLNESS

## Slide 22
Prohibit use of artificial eyelash, synthetic nail, and other beauty accessories that can fall into the products.
Hair combing is allowed only in the locker room.
Prohibit use of rings, earring, and other jewelries in production area
REGULATION IN PRODUCTION AREA

## Slide 23
“No Eating”, “No Drinking”, “No Smoking”, and “No Chewing Gum” policy shall be strictly implemented as well as no spitting on the floor.
Food shall not be kept in production, warehouse or laboratory area.
No Smoking
No Eating,
No Drinking
NO EATING, DRINKING & SMOKING

## Slide 24
PREMISES SANITATION

## Slide 25
Cleaning and sanitation alone will not assure a hygienic standard in production. Process hygiene as well as personal hygiene are important factors.
Buildings / facilities should be so constructed that clean and unclean processes and products do not mix.
A well-planned, well-executed and controlled cleaning and sanitation programme for rooms, machines and equipment is very important to achieve a hygienic standard.
The cleaning program must be performed regularly, dependent on the demand for cleaning in the specific areas. The requirements for cleaning have to be defined before establishing the cleaning program.
GOOD HOUSEKEEPING PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
General principle of good housekeeping can be found in the attached hyperlink documents

## Slide 26
The design of the premises depends on the manufacturing activities. However, in general terms, all areas should be designed in such a way that prevents the build-up of dirt and dust.
The plant facilities shall:
provide sufficient space for equipment and storage of materials as necessary for the maintenance of sanitary operations and safe production.
provide adequate lighting, ventilation or control equipment to minimize contamination.
have an effective pest control program.
check pests and pest infestation on a regular basis.
provide, where necessary, adequate screening or other protection against pests.
PREMISES DESIGN (1)
Notes: <number>
<footer>
<header>
<date/time>
Plant buildings and structures shall be suitable in size, construction, and design to facilitate maintenance and sanitary operations.

## Slide 27
Buildings / facilities should be so constructed that :
floors, walls, and ceilings may be adequately cleaned and kept clean, and kept in good repair;
floor must be hard, smooth and impervious, sloping sufficiently towards a drain thus allowing cleaning with water;
the grounds shall be kept in a condition that will protect the product against contamination, and to include proper storage of equipment, removing litter and waste;
drains are kept to a minimum amount. Their design must prevent the possibility of back-flow. Open channels should be easy to clean and sanitize.
PREMISES DESIGN (2)

## Slide 28
In addition:
There must be a written cleaning and sanitization procedure indicating who is responsible for its execution, the materials used and methodology. The procedure should be appropriate to the area being cleaned.
There should also be a written record of cleaning that has been performed.
There should be maximum protection against the entry of insects or other animals. For loading bays in particular, there needs to be protection against the weather and flying animals.
Air curtain
PREMISES DESIGN (3)

## Slide 29
Facilities must be well maintained to prevent any contamination to get into the production area.
Doors and windows must always be kept closed at all times in the production area. Screens must be installed on windows or any other openings.
X
X


CLOSED DOORS & WINDOW

## Slide 30
Each plant shall be equipped with adequate sanitary facilities including, but not limited to:
  Water supply
  Plumbing
  Toilet facilities
  Hand washing facilities
  Rubbish disposal
  Changing facility or locker
which should be sufficient, adequate in size and design, and properly installed for easy cleaning and sanitation processes.
SANITATION FACILITIES

## Slide 31
Water is the main source of product contamination.
The water supply shall be sufficient for the operations intended and shall be derived from an adequate source.
Plumbing shall be of adequate size and design and adequately installed and maintained to:
  carry sufficient quantities of water to required locations
  properly convey sewage and liquid disposable waste
  provide adequate floor drainage in all areas
  ensure that there is no back-flow from, or cross-connection between piping systems
Sanitation Facilities
WATER SUPPLY & PLUMBING
Notes: <number>
<footer>
<header>
<date/time>
Plumbing shall be of adequate size and design and adequately installed and maintained to:
  carry sufficient quantities of water to required locations
  properly convey sewage and liquid disposable waste from the plant.
  provide adequate floor drainage in all areas where floors are subject to flooding-type cleaning or where normal operations release or discharge water or liquid waste on the floor.
  provide that there is no back-flow from, or cross-connection between piping systems that discharge waste water or sewage and piping systems that carry water for food or food manufacturing.

## Slide 32
Adequate employee’s washing and well ventilated toilet facilities should be provided and separated from the production area.
  Must be kept clean at all times
  Well maintained
  With adequate supply of water
  Provided with soap, hand dryer or paper towel
  Used properly by all employees
Sanitation Facilities
HAND WASHING & TOILET

## Slide 33
Waste material should be placed in suitable container and regularly collected for disposal outside the production areas.
  Regular & timely collection of garbage
  Garbage bins must be properly covered at all times
  No food wrapper to be thrown in garbage cans inside the production area
  Do not use product shipping cases as garbage bins
Sanitation Facilities
RUBBISH DISPOSAL

## Slide 34
Suitable changing facilities or locker should be provided at appropriate location for the storage of employees’ clothing and personal belongings
Personal belonging shall be kept in lockers or drawers.
Sanitation Facilities
CHANGING ROOM(S)

## Slide 35
A Clean Workplace is High in QUALITY;
A Clean Workplace is High in PRODUCTIVITY;
A Clean Workplace Keeps COSTS Down;
A Clean Workplace Saves TIME;
A Clean Workplace Ensures EFFICIENT Delivery;
A Clean Workplace Provides HEALTHY environment;
A Clean Workplace is SAFE for people to work in;
A Clean Workplace is High in MORALE.
Before cleaning program
After cleaning program
GOOD HOUSEKEEPING ADVANTAGES

## Slide 36
EQUIPMENT
SANITATION

## Slide 37
The main principle for equipment should be that it is easy to dismantle or remove to facilitate cleaning by non-corrosive materials.
Design, type, size and installation of equipment shall be in such a way as to avoid and prevent any contamination during use.
When choosing and buying machines, hygienic production and possibilities for cleaning and disinfection must be considered.
Contamination is a leading cause of product failure. The maintenance personnel and others involved in production need to understand the destructive nature of contamination and realize the benefits in removing contamination from their facilities.
SANITATION PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
Principles of equipment sanitation :
The main principle for equipments should be that it is easy to dismantle or remove to facilitate cleaning and that it should be made of non-corrosive materials.
Design, type, size and installation of equipment shall be in such a way that any contamination that might occur during manufacturing such as lubricants, dust, metals is prevented, avoided and minimized
Cleaning and disinfection will often be complicated or impossible because of the complex construction of machines and when choosing and buying machines, hygienic production and possibilities for cleaning and disinfection must be considered.
Contamination is a leading cause of machinery failure. Maintenance and reliability professionals need to comprehend the destructive nature of contamination and realize the benefits in removing contamination from their facilities. If foreign materials enter your system, critical responses are necessary to minimize the effects of destructive contaminants.

## Slide 38
Cleaning operations shall be performed in a manner to prevent contamination of materials and products.
Only cleaning compounds and sanitizers authorized shall be used for cleaning.
All cleaning compounds and sanitizers shall be properly labelled and stored in a locked compartment, away from production and food storage areas.
Cleaning equipment and tools shall be supplied and be readily available for use.
Equipment and utensils should be kept clean.
The written instruction for cleaning and sanitation for each equipments and utensils should be provided.
CLEANING PRACTICES
Notes: <number>
<footer>
<header>
<date/time>
Cleaning practices :
Cleaning operations shall be performed in a manner to prevent contamination of materials and products. Cleaning methods shall be done in a manner to minimize the potential for product contamination.
Only cleaning compounds and sanitizers authorized for product contact surfaces shall be used for cleaning. Appropriate verification procedures or testing shall be done periodically to insure that the concentration of Clean-In-Place (CIP) and other cleaning chemicals are consistent with the product labeling.
When not in use, all cleaning compounds and sanitizers shall be properly labeled and stored in a locked compartment, away from production and food storage areas..
Cleaning equipment and tools shall be supplied and be readily available for use. All cleaning equipment shall be maintained and stored in such a way as not to contaminate foods or food equipment.
Equipment and utensils should be kept clean
  Vacuum or wet cleaning methods are preferred. Compressed air and brushes should be used with care and avoided if possible as they increase the risk of product contamination
  Standard operating procedures must be followed for cleaning and sanitizing of major machines
Cleaning and sanitization procedures :
  shall be validated as to its
  effectiveness in removing contaminants and residues.

## Slide 39
Written SOP’s shall be established specifying:
areas, equipment to be cleaned
cleaning and sanitization procedure for each area, equipment
cleaning and sanitization frequency such as between individual batches, change over from one product to another, plant shutdown or new equipment
precautions to minimize contamination and spread of microorganisms
personnel assigned to do the cleaning
CLEANING PROCEDURE
Notes: <number>
<footer>
<header>
<date/time>
Guidance for work instruction for cleaning procedure is attached in hyperlink documents

## Slide 40
1. Foam: Foam is produced through the introduction of air into a detergent solution as it is sprayed onto the surface to be cleaned. Foam cleaning will increase the contact time of the chemical solutions, allowing for improved cleaning with less mechanical force and temperature.
2. High Pressure: High pressure cleaning is used to increase the mechanical force, aiding in soil removal. In high pressure cleaning chemical detergents are often used along with increased temperature to make soil removal more effective.
3. Clean in Place (CIP): CIP cleaning is utilized to clean interior surfaces of tanks and pipelines of liquid process equipment. A chemical solution is circulated through a circuit of tanks and or lines then returned to a central reservoir allowing for reuse of the chemical solution. Time, temperature, and mechanical force are manipulated to achieve maximum cleaning.
4. Clean Out Of Place (COP): COP cleaning is utilized to clean tear down parts of fillers and parts of other equipment which require disassembly for proper cleaning. Parts removed for cleaning are placed in a circulation tank and cleaned using a heated chemical solution and agitation.
5. Mechanical: Mechanical cleaning normally involves the use of a brush either by hand or a machine such as a floor scrubber. Mechanical cleaning uses friction for food soil removal.
CLEANING METHOD

## Slide 41
FACTOR THAT INFLUENCE CLEANING
There are 4 interrelated factors which affect the overall cleaning process.
When designing cleaning procedures these factors need to be carefully considered:
  Cleaning time
  Temperature
  Chemical being used
  Mechanical forces
Notes: <number>
<footer>
<header>
<date/time>
There are 4 interrelated factors which effect the overall cleaning process. When designing cleaning procedures these factors need to be carefully considered.
Time: The longer a cleaning solution remains in contact with the equipment surface, the greater the amount of dirt that is removed. Increasing time reduces the chemical concentration requirements.
Temperature: Dirt are affected to varying degrees by temperature. In the presence of a cleaning solution most dirt become more readily soluble as the temperature is increased.
Chemical Concentrations: Chemical concentrations vary depending upon the chemical itself, type of dirtl, and the equipment to be cleaned. Concentration will normally be reduced as time and temperature are increased.
Mechanical Force: Mechanical force can be simple hand scrubbing with a brush or as complex as turbulent flow and pressure inside a pipeline. Mechanical force aids in dirt removal and typically reduces time, temperature, and concentration requirements.

## Slide 42
The following are the typical considerations when designing a cleaning and sanitization procedure of processing equipment:
  the factors that influence cleaning (time, temperature, chemical concentration, and mechanical force),
  the method of cleaning,
  the type of dirt to be removed
FUNDAMENTAL OF CLEANING
Notes: <number>
<footer>
<header>
<date/time>
The following is the typical procedure used when cleaning processing equipment, such as
The factors that influence cleaning (time, temperature, chemical concentration, and mechanical force),
the method of cleaning, and
the dirt type to be removed will ultimately determine the cleaning procedures selected for use.
Several guidance for cleaning process:
Clearance for cleaning: It is recommended that each person in processing be responsible for clearing the area concerned as this tends to intensify discipline regarding tidiness and hygiene. The purpose of clearance after work is to prepare an easy and quick cleaning procedure. Clearance implies removal of all items which may retard performance.
Pre-Rinse: Dirty equipment surfaces are rinsed with warm water to remove the gross amounts of loose dirt.
Cleaning Cycle: Removal of residual product from equipment surfaces through manipulation of the four basic cleaning factors and the method of cleaning. Typically alkaline chemical solutions are used for the cleaning cycle.
Rinse: Rinsing of all surfaces with cold to hot water, depending upon the temperature of the cleaning cycle, to thoroughly remove all remaining chemical solution and product residues.
Acid Rinse: A mild acid rinse of the equipment neutralizes any alkaline residues left and removes any mineral dirt present.
Sanitize: All equipment surfaces are rinsed or flooded with a sanitizing agent. Time and concentration are critical for optimum results.

## Slide 43
There are two classes of cleaning compounds :
  acid cleaners, and
  alkaline cleaners
Chemical formulations for acid and alkaline compounds may vary according to the following:
  chemical dispensing method
  method of cleaning
  type of processing equipment to be cleaned
CLEANING COMPOUNDS
Notes: <number>
<footer>
<header>
<date/time>
Cleaning coumpound description :
There are two classes of cleaning compounds, acid and alkaline.
Chemical formulations for acid and alkaline compounds vary widely providing for selection flexibility when considering sanitation procedures, types of processing equipment to be cleaned, chemical dispensing, and method of cleaning.
Acid cleaners :
  Phosphoric Acid: Phosphoric acid provides the bulk of the acidity in most acid cleaners. Phosphoric solublizes minerals well and is less corrosive to metals than most other acids.
  Other Acidulants: Acetic, hydroxyacetic, citric, sulfamic, and nitric acids are also used in many cleaners to a varying degree. Nitric acid use has expanded greatly due mainly to cost, however nitric is very effective in the removal of tough mineral deposits in heat exchangers and evaporators.
  Surface Active Agents (Surfactants): Surfactants help break down the surface tension of soils to improve removal. Once the food soil is removed the surfactant forms a colloidal suspension with the soil, keeping it water soluble to prevent it from redepositing on the equipment surfaces.
Alkaline cleaners :
  Sodium or Potassium Hydroxide: Hydroxides provide the largest portion of alkalinity and effectively saponify fats and peptize proteins for removal
  Sodium Metasilicate: Aids in emulsifying and soil suspension along with protecting against metal corrosion.
  Complex Phosphates: Phosphates primary function is to soften the water by chelating (binding up) the calcium and magnesium hardness. This allows for better cleaning effectiveness and reduces mineral deposits. Phosphates will also aid in emulsifying food soils.
  Surface Active Agents (Surfactants): Surfactants help break down the surface tension of soils to improve removal. Once the food soil is removed the surfactant forms a colloidal suspension with the soil, keeping it water soluble to prevent it from redepositing on the equipment surfaces.
  Chlorine: Chlorine is added to many chemical formulations to help in peptizing proteins.

## Slide 44
Cleaning and sanitization records/log books must be kept for all manufacturing areas. The operator shall record the area/equipment cleaned and sanitized (as necessary), sign the record and to be countersigned by another individual who
checks the cleanliness of
the equipment/area.
CLEANING RECORD

## Slide 45
The main objective of a cleaning program is to control microbial activity. Although an adequate cleaning program will eliminate nearly all the soil present, however, it will not destroy or remove all the micro-organisms.
And this requires a second step “sanitation”
Sanitation methods can be divided into two groups:
1. Non-chemical disinfection methods
2. Chemical disinfection methods
SANITATION PRINCIPLES
Notes: <number>
<footer>
<header>
<date/time>
Sanitation methods :
Non chemical method
  In many cases hot water (900 C or more) or steam is the best way for sanitation purpose, but it may be inconvenient or impractical due to the following reasons :
    Providing hot water or steam is expensive and may cause materials to deteriorate and equipment to distort.
    If steam is used it will take considerable time to heat and cool equipment. It may cause baking-on product and other residues.
    Visibility is reduced in the environment thus reducing the effectiveness of the sanitizing procedures.
    Finally it gives condensation problems.
  Insufficient heating may result in the incubation of microorganisms in inaccessible parts of the machines and the equipment.
Chemical method
  The most essential for an effective chemical sanitation program is a clean surface. Consequently, to achieve microbial control the cleaning and sanitation program must be thorough, compatible and totally effective.
  The choice of chemical disinfectants is determined by the following considerations:
    Public health regulations
    Spectrum of effectiveness, i.e. ability to kill many types of microorganisms
    Must be efficient under the conditions of use
    Quick action
    Presence or absence of organic matter
    Corrosive properties
    Type of processing area and type of surface to be disinfected
    Non-toxic and gentle to the skin
    Inexpensive
    Must not affect the odour or flavour of the product on the equipment
    Must be easily rinsed away and leave no toxic residues
    Easy to dispense and to handle
    Must be safe in use and must not affect the operators who use it.
  Manufacturers offer a large number of disinfectants, each claimed to be the best on the market. Nevertheless the only ones suitable for the cosmetic industry contain chemicals of one of the following groups:
    Chlorine and chlorine-releasing compounds
    Quarternary ammonium compounds
    Amphoteric (ampholytic) compounds
    Phenolic compounds
    Peracetic acid

## Slide 46
A well-planned, well-executed and controlled cleaning and sanitation program for rooms, machines, equipment and working area is very important to achieve a hygienic standard.
Cleaning and sanitation alone, however, will not assure a hygienic standard in production. Process hygiene as well as personal hygiene are equally important factors.
A well planned working routine may assure a better standard of cleanliness during processing.
Adequate personal hygiene assures the overall cleaning process. Deterioration of the cleaning standard may occur if micro-organisms are transmitted to well-cleaned surfaces from unwashed hands before processing starts.
<number>
CONCLUSION

## Slide 47
Trainer Manual of Sanitation & Hygiene
Contamination & Good Housekeeping
Pest Control Program
Work Instruction: Cleaning Guidance
RELATED HYPERLINK DOCUMENTS

## Slide 48
ASEAN Guideline for Cosmetic GMP, 2003
WHO Basic Principle of GMP : Sanitation & Hygiene, 2000
Bishop, Basic Principle of Sanitation, N.E.M. Business Solutions, 1997
Health Services Agency, County of Santa Cruz, Cross Contamination, 1999
Barwa N. S., Implementation of Clean Production in Cosmetic Industry, 2002
www.fao.org
www.maintenanceconference.com
REFERENCES

## Slide 49
Pest and microorganism will run away when we do good practices of sanitation & hygiene
Thank you for your kind attention